## Slide 1: Computer Performance
More practice
31 August 2022
Cheryl Resch

## Slide 2
A program P is compiled with two different compilers on a platform with a clock rate of 2 GHz. Compiler A results in an instruction count of 1e6 and an execution time of 1.1 ms. Compiler B results in an instruction count of 1.2e6 and an execution time of 1.5 ms.
What is the average CPI for the program on each compiler?

## Slide 3
A program P is compiled with two different compilers on a platform with a clock rate of 2 GHz. Compiler A results in an instruction count of 1e6 and an execution time of 1.1 ms. Compiler B results in an instruction count of 1.2e6 and an execution time of 1.5 ms.
What is the average CPI for the program on each compiler?
Compiler A – (2e9 cycles/second * 1.1e-3 seconds) / ( 1e6 instructions ) = 2.2 cycles/instruction
Compiler B - (2e9 cycles/second * 1.5e-3 seconds) / (1.2e6 instructions ) = 2.5 cycles/instruction
What is the speedup for compiler A compared to compiler B?

## Slide 4
A program P is compiled with two different compilers on a platform with a clock rate of 2 GHz. Compiler A results in an instruction count of 1e6 and an execution time of 1.1 ms. Compiler B results in an instruction count of 1.2e6 and an execution time of 1.5 ms.
What is the average CPI for the program on each compiler?
Compiler A – (2e9 cycles/second * 1.1e-3 seconds) / ( 1e6 instructions ) = 2.2 cycles/instruction
Compiler B - (2e9 cycles/second * 1.5e-3 seconds) / (1.2e6 instructions ) = 2.5 cycles/instruction
What is the speedup for compiler A compared to compiler B?
1.5/1.1 = 1.36

## Slide 5
A program P is compiled with two different compilers on a platform with a clock rate of 2 GHz. Compiler A results in an instruction count of 1e6 and an execution time of 1.1 ms. Compiler B results in an instruction count of 1.2e6 and an execution time of 1.5 ms.
A new compiler is developed that compiles program P and this results in 6e5 instructions and a CPI of 2.0. What is the speedup for this compiler compared to Compiler A and compared to Compiler B?

## Slide 6
A program P is compiled with two different compilers on a platform with a clock rate of 2 GHz. Compiler A results in an instruction count of 1e6 and an execution time of 1.1 ms. Compiler B results in an instruction count of 1.2e6 and an execution time of 1.5 ms.
A new compiler is developed that compiles program P and this results in 6e5 instructions and a CPI of 2.0. What is the speedup for this compiler compared to Compiler A and compared to Compiler B?
Execution time on new compiler = (6e5 instructions* 2 cycles/instruction) / (2e9 cycles/second) = 6e-4 seconds = 0.6 ms
Speedup A = 1.1/0.6 = 1.83
Speedup B = 1.5/0.6 = 2.5

## Slide 7
A computer with a clock rate of 1 GHz executes branch instructions with an average CPI of 2, memory load/store instructions with an average CPI of 5, and arithmetic instructions with an average CPI of 3.
Program P consists of 30% branch instructions, 20% memory load/store operations, and 50% arithmetic instructions.
What is the average CPI for program P?

## Slide 8
A computer with a clock rate of 1 GHz executes branch instructions with an average CPI of 2, memory load/store instructions with an average CPI of 5, and arithmetic instructions with an average CPI of 3.
Program P consists of 30% branch instructions, 20% memory load/store operations, and 50% arithmetic instructions.
What is the average CPI for program P?
CPIavg = 0.3*2 + 0.2*5 + 0.5*3 = 0.6+1+1.5 = 3.1 cycles/instruction
What is the execution time if P has 15000 instructions?

## Slide 9
A computer with a clock rate of 1 GHz executes branch instructions with an average CPI of 2, memory load/store instructions with an average CPI of 5, and arithmetic instructions with an average CPI of 3.
Program P consists of 30% branch instructions, 20% memory load/store operations, and 50% arithmetic instructions.
What is the average CPI for program P?
CPIavg = 0.3*2 + 0.2*5 + 0.5*3 = 0.6+1+1.5 = 3.1 cycles/instruction
What is the execution time if P has 15000 instructions?
t = (15000 instructions * 3.1 cycles/instruction) / 1e9 cycles/second = 4.65e-5 seconds
What is the speedup if the clock is improved to 1.5 GHz and memory load/store instructions are improved to CPI=4?

## Slide 10
A computer with a clock rate of 1 GHz executes branch instructions with an average CPI of 2, memory load/store instructions with an average CPI of 5, and arithmetic instructions with an average CPI of 3.
Program P consists of 30% branch instructions, 20% memory load/store operations, and 50% arithmetic instructions.
What is the average CPI for program P?
CPIavg = 0.3*2 + 0.2*5 + 0.5*3 = 0.6+1+1.5 = 3.1 cycles/instruction
What is the execution time if P has 15000 instructions?
t = (15000 instructions * 3.1 cycles/instruction) / 1e9 cycles/second = 4.65e-5 seconds
What is the speedup if the clock is improved to 1.5 GHz and memory load/store instructions are improved to CPI=4?
CPI avg new = 0.3*2 + 0.2+4 + 0.5*3 = 0.6+0.8+1.5 = 2.9 cycles/instruction
tnew = (15000 instructions * 2.9 cycles/instruction) / 1.5e9 cycles/second = 2.9e-5 seconds
Speedup = 4.65/2.9 = 1.603