## Slide 1: November 17 Discussion
CDA 3101

## Slide 2: Examlet 6
Average memory access time for look aside and look through cache
Direct mapped, set associative, and fully associative
  Calculate size of fields
  Determine mapping into cache
  All the example problems we went over in class and discussion 
Virtual memory
  Map virtual memory address to page map table
  Translate virtual address to physical address

## Slide 3: Example Problem 2
Consider a system with a main memory access time of 100 ns is supported by an L1 cache having a 10 ns access time and a hit rate of 90% and an L2 cache having a 20 ns access time and a hit rate of 80%
What is the average memory access time for a look aside cache?
What is the average memory access time for a look through cache?

## Slide 4: Example Problem 2
Consider a system with a main memory access time of 100 ns is supported by an L1 cache having a 10 ns access time and a hit rate of 90% and an L2 cache having a 20 ns access time and a hit rate of 80%
What is the average memory access time for a look aside cache?
AMAT = 10(0.9) + 0.1*(20*0.8 + 100*0.2) = 12.6 ns
What is the average memory access time for a look through cache?

## Slide 5: Example Problem 2
Consider a system with a main memory access time of 100 ns is supported by an L1 cache having a 10 ns access time and a hit rate of 90% and an L2 cache having a 20 ns access time and a hit rate of 80%
What is the average memory access time for a look aside cache?
AMAT = 10(0.9) + 0.1*(20*0.8 + 100*0.2) = 12.6 ns
What is the average memory access time for a look through cache?
AMAT = 10 + 0.1(20 + 0.2*100) = 14 ns

## Slide 6: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
How many bits wide is the address?
How many bits wide is the offset field?
How many bits describe the block?

## Slide 7
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes
How many bits wide is the address?
log(65536) = 16
How many bits wide is the offset field?
log(512) = 9
How many bits describe the block?
16 - 9 = 7 bits

## Slide 8: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
The system has a cache that is 8192 bytes.
How many lines does the cache have?

## Slide 9: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
The system has a cache that is 8192 bytes.
How many lines does the cache have?
(8192 bytes/cache) / (512 bytes/line) = 16 lines/cache

## Slide 10: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
The system has a cache that is 8192 bytes.
How many lines does the cache have?
(8192 bytes/cache) / (512 bytes/line) = 16 lines/cache
If the cache is fully associative, into how many possible lines can a block be placed?

## Slide 11: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
The system has a cache that is 8192 bytes.
How many lines does the cache have?
(8192 bytes/cache) / (512 bytes/line) = 16 lines/cache
If the cache is fully associative, into how many possible lines can a block be placed?
16 – any block can go to any line
How many bits are in the tag field for a fully associative cache?

## Slide 12: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
The system has a cache that is 8192 bytes.
How many lines does the cache have?
(8192 bytes/cache) / (512 bytes/line) = 16 lines/cache
If the cache is fully associative, into how many possible lines can a block be placed?
16 – any block can go to any line
How many bits are in the tag field for a fully associative cache?
16-9 = 7

## Slide 13: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
The system has a cache that is 8192 bytes.
How many lines does the cache have?
(8192 bytes/cache) / (512 bytes/line) = 16 lines/cache
If the cache is direct mapped, into how many possible lines can a block be placed?

## Slide 14: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
The system has a cache that is 8192 bytes.
How many lines does the cache have?
(8192 bytes/cache) / (512 bytes/line) = 16 lines/cache
If the cache is direct mapped, into how many possible lines can a block be placed?
1 – each block maps to one line in the cache

## Slide 15: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
The system has a cache that is 8192 bytes.
How many lines does the cache have?
(8192 bytes/cache) / (512 bytes/line) = 16 lines/cache
If the cache is direct mapped, into how many possible lines can a block be placed?
1 – each block maps to one line in the cache
How many bits are in the line field and the tag field?

## Slide 16: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
The system has a cache that is 8192 bytes.
How many lines does the cache have?
(8192 bytes/cache) / (512 bytes/line) = 16 lines/cache
If the cache is direct mapped, into how many possible lines can a block be placed?
1 – each block maps to one line in the cache
How many bits are in the line field and the tag field?
16 lines, so log(16) = 4 bits in the line field (4 bits are needed to count to 16)
16-9-4 = 3 bits in the tag field

## Slide 17: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
The system has a cache that is 8192 bytes.
How many lines does the cache have?
(8192 bytes/cache) / (512 bytes/line) = 16 lines/cache
If the cache is 2-way set associative, into how many possible lines can a block be placed?

## Slide 18: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
The system has a cache that is 8192 bytes.
How many lines does the cache have?
(8192 bytes/cache) / (512 bytes/line) = 16 lines/cache
If the cache is 2-way set associative, into how many possible lines can a block be placed?
2 – a block will map to a set, and that set has two lines

## Slide 19: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
The system has a cache that is 8192 bytes.
How many lines does the cache have?
(8192 bytes/cache) / (512 bytes/line) = 16 lines/cache
If the cache is 2-way set associative, into how many possible lines can a block be placed?
2 – a block will map to a set, and that set has two lines
How many bits are in the set and tag fields?

## Slide 20: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
The system has a cache that is 8192 bytes.
How many lines does the cache have?
(8192 bytes/cache) / (512 bytes/line) = 16 lines/cache
If the cache is 2-way set associative, into how many possible lines can a block be placed?
2 – a block will map to a set, and that set has two lines
How many bits are in the set and tag fields?
(16 lines/cache) / (2 lines/set) = 8 sets/cache
log(8) = 3, set field is 3 bits
Tag = 16-9-3 = 4 bits

## Slide 21
Page | Frame | Valid
0000 | 011 | 1
0001 |  | 0
0010 | 010 | 1
0011 |  | 0
0100 | 100 | 1
0101 |  | 0
0110 | 111 | 1
0111 |  | 0
1000 | 000 | 1
1001 |  | 0
1010 |  | 0
1011 | 101 | 1
1100 |  | 0
1101 |  | 0
1110 | 001 | 1
1111 | 110 | 1
Page Map Table
Pages in virtual memory are mapped to frames in physical memory (main memory)

## Slide 22
Page | Frame | Valid
0000 | 011 | 1
0001 |  | 0
0010 | 010 | 1
0011 |  | 0
0100 | 100 | 1
0101 |  | 0
0110 | 111 | 1
0111 |  | 0
1000 | 000 | 1
1001 |  | 0
1010 |  | 0
1011 | 101 | 1
1100 |  | 0
1101 |  | 0
1110 | 001 | 1
1111 | 110 | 1
Page Map Table
A system has 212 bytes of virtual address space. A frame is 28 bytes. Physical address space (main memory) is 211 bytes
How many bits are in the virtual address?
How many bits are in the physical address?

## Slide 23
Page | Frame | Valid
0000 | 011 | 1
0001 |  | 0
0010 | 010 | 1
0011 |  | 0
0100 | 100 | 1
0101 |  | 0
0110 | 111 | 1
0111 |  | 0
1000 | 000 | 1
1001 |  | 0
1010 |  | 0
1011 | 101 | 1
1100 |  | 0
1101 |  | 0
1110 | 001 | 1
1111 | 110 | 1
Page Map Table
A system has 212 bytes of virtual address space. A frame is 28 bytes. Physical address space (main memory) is 211 bytes
How many bits are in the virtual address? log(212) = 12
How many bits are in the physical address? log(211) = 11
How many bits are in the offset field?
How many bits are in the page field of the virtual address?
How many bits are in the frame field of the physical address?

## Slide 24
Page | Frame | Valid
0000 | 011 | 1
0001 |  | 0
0010 | 010 | 1
0011 |  | 0
0100 | 100 | 1
0101 |  | 0
0110 | 111 | 1
0111 |  | 0
1000 | 000 | 1
1001 |  | 0
1010 |  | 0
1011 | 101 | 1
1100 |  | 0
1101 |  | 0
1110 | 001 | 1
1111 | 110 | 1
Page Map Table
A system has 212 bytes of virtual address space. A frame is 28 bytes. Physical address space (main memory) is 211 bytes
How many bits are in the virtual address? log(212) = 12
How many bits are in the physical address? log(211) = 11
How many bits are in the offset field? log(28) = 8
How many bits are in the page field of the virtual address? 12-8 = 4
How many bits are in the frame field of the physical address? 11-8 = 3

## Slide 25
Page | Frame | Valid
0000 | 011 | 1
0001 |  | 0
0010 | 010 | 1
0011 |  | 0
0100 | 100 | 1
0101 |  | 0
0110 | 111 | 1
0111 |  | 0
1000 | 000 | 1
1001 |  | 0
1010 |  | 0
1011 | 101 | 1
1100 |  | 0
1101 |  | 0
1110 | 001 | 1
1111 | 110 | 1
Page Map Table
A system has 212 bytes of virtual address space. A frame is 28 bytes. Physical address space (main memory) is 211 bytes
How many bits are in the virtual address? log(212) = 12
How many bits are in the physical address? log(211) = 11
How many bits are in the offset field? log(28) = 8
How many bits are in the page field of the virtual address? 12-8 = 4
How many bits are in the frame field of the physical address? 11-8 = 3
The virtual address 0xBAD is requested. Is this is a hit in the page map table? What does this mean?

## Slide 26
Page | Frame | Valid
0000 | 011 | 1
0001 |  | 0
0010 | 010 | 1
0011 |  | 0
0100 | 100 | 1
0101 |  | 0
0110 | 111 | 1
0111 |  | 0
1000 | 000 | 1
1001 |  | 0
1010 |  | 0
1011 | 101 | 1
1100 |  | 0
1101 |  | 0
1110 | 001 | 1
1111 | 110 | 1
Page Map Table
A system has 212 bytes of virtual address space. A frame is 28 bytes. Physical address space (main memory) is 211 bytes
How many bits are in the virtual address? log(212) = 12
How many bits are in the physical address? log(211) = 11
How many bits are in the offset field? log(28) = 8
How many bits are in the page field of the virtual address? 12-8 = 4
How many bits are in the frame field of the physical address? 11-8 = 3
The virtual address 0xBAD is requested. Is this is a hit in the page map table? What does this mean?
0xBAD = 101110101101 = 1011 10101101
This is a hit, because the valid bit in this row is 1 and it is mapped to a frame
This means that this page is in main memory

## Slide 27
Page | Frame | Valid
0000 | 011 | 1
0001 |  | 0
0010 | 010 | 1
0011 |  | 0
0100 | 100 | 1
0101 |  | 0
0110 | 111 | 1
0111 |  | 0
1000 | 000 | 1
1001 |  | 0
1010 |  | 0
1011 | 101 | 1
1100 |  | 0
1101 |  | 0
1110 | 001 | 1
1111 | 110 | 1
Page Map Table
A system has 212 bytes of virtual address space. A frame is 28 bytes. Physical address space (main memory) is 211 bytes
How many bits are in the virtual address? log(212) = 12
How many bits are in the physical address? log(211) = 11
How many bits are in the offset field? log(28) = 8
How many bits are in the page field of the virtual address? 12-8 = 4
How many bits are in the frame field of the physical address? 11-8 = 3
The virtual address 0xBAD is requested. Is this is a hit in the page map table? What does this mean?
0xBAD = 101110101101 = 1011 10101101
Map the virtual address to a physical address

## Slide 28
Page | Frame | Valid
0000 | 011 | 1
0001 |  | 0
0010 | 010 | 1
0011 |  | 0
0100 | 100 | 1
0101 |  | 0
0110 | 111 | 1
0111 |  | 0
1000 | 000 | 1
1001 |  | 0
1010 |  | 0
1011 | 101 | 1
1100 |  | 0
1101 |  | 0
1110 | 001 | 1
1111 | 110 | 1
Page Map Table
A system has 212 bytes of virtual address space. A frame is 28 bytes. Physical address space (main memory) is 211 bytes
How many bits are in the virtual address? log(212) = 12
How many bits are in the physical address? log(211) = 11
How many bits are in the offset field? log(28) = 8
How many bits are in the page field of the virtual address? 12-8 = 4
How many bits are in the frame field of the physical address? 11-8 = 3
The virtual address 0xBAD is requested. Is this is a hit in the page map table? What does this mean?
0xBAD = 101110101101 = 1011 10101101
Map the virtual address to a physical address
Page 1011 maps to frame 101
Physical address is 101 10101101