## Slide 1: April 5 Discussion
CDA 3101

## Slide 2: Examlet 6
Cache memory compared to registers or main memory
Average memory access time for look aside and look through cache
Direct mapped, set associative, and fully associative
  Calculate size of fields
  Determine mapping into cache
  All the example problems we went over in class and discussion 

## Slide 3: Why Do We Have Cache?
Registers
  Fast access
  Expensive per byte
  On chip, size (number of bytes)
  Data operated on by ALU must be in registers
  Have to transfer from main memory
Main Memory
  Slower access
  Less expensive per byte
  Large
Cache?

## Slide 4: Why Do We Have Cache?
Registers
  Fastest access
  Most expensive per byte
  On chip, size (number of bytes) is small
  Data operated on by ALU must be in registers
  Have to transfer from main memory
Main Memory
  Slower access
  Less expensive per byte
  Large
Cache
  Used to make transfer to registers faster
  Faster access than main memory
  More expensive per byte than main memory
  Smaller than main memory

## Slide 5: Why Do We Have Cache?
Used to make transfer to registers faster
Faster access than main memory
More expensive per byte than main memory
Smaller than main memory
Cache is a subset of main memory
Put items in cache that are likely to be accessed
  temporal locality – recently accessed items may be accessed again
  spatial locality – items near recently accessed items may be accessed

## Slide 6: Example Problem 2
Consider a system with a main memory access time of 100 ns is supported by an L1 cache having a 10 ns access time and a hit rate of 90% and an L2 cache having a 20 ns access time and a hit rate of 80%
What is the average memory access time for a look aside cache?
What is the average memory access time for a look through cache?

## Slide 7: Example Problem 2
Consider a system with a main memory access time of 100 ns is supported by an L1 cache having a 10 ns access time and a hit rate of 90% and an L2 cache having a 20 ns access time and a hit rate of 80%
What is the average memory access time for a look aside cache?
AMAT = 10(0.9) + 0.1*(20*0.8 + 100*0.2) = 12.6 ns
What is the average memory access time for a look through cache?

## Slide 8: Example Problem 2
Consider a system with a main memory access time of 100 ns is supported by an L1 cache having a 10 ns access time and a hit rate of 90% and an L2 cache having a 20 ns access time and a hit rate of 80%
What is the average memory access time for a look aside cache?
AMAT = 10(0.9) + 0.1*(20*0.8 + 100*0.2) = 12.6 ns
What is the average memory access time for a look through cache?
AMAT = 10 + 0.1(20 + 0.2*100) = 14 ns

## Slide 9: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
How many bits wide is the address?
How many bits wide is the offset field?
How many bits describe the block?

## Slide 10
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes
How many bits wide is the address?
log(65536) = 16
How many bits wide is the offset field?
log(512) = 9
How many bits describe the block?
16 - 9 = 7 bits

## Slide 11: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
The system has a cache that is 8192 bytes.
How many lines does the cache have?

## Slide 12: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
The system has a cache that is 8192 bytes.
How many lines does the cache have?
(8192 bytes/cache) / (512 bytes/line) = 16 lines/cache

## Slide 13: What Causes Cache Misses?
Compulsory misses – cache is empty when a process starts
Capacity misses – the cache is full, based on size of cache
Conflict – more than one block mapping to the same block
  Fully associative – no conflict misses – any block can go anywhere
  Direct associative – highest rate of conflict misses

## Slide 14: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
The system has a cache that is 8192 bytes.
How many lines does the cache have?
(8192 bytes/cache) / (512 bytes/line) = 16 lines/cache
If the cache is fully associative, into how many possible lines can a block be placed?

## Slide 15: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
The system has a cache that is 8192 bytes.
How many lines does the cache have?
(8192 bytes/cache) / (512 bytes/line) = 16 lines/cache
If the cache is fully associative, into how many possible lines can a block be placed?
16 – any block can go to any line
How many bits are in the tag field for a fully associative cache?

## Slide 16: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
The system has a cache that is 8192 bytes.
How many lines does the cache have?
(8192 bytes/cache) / (512 bytes/line) = 16 lines/cache
If the cache is fully associative, into how many possible lines can a block be placed?
16 – any block can go to any line
How many bits are in the tag field for a fully associative cache?
16-9 = 7

## Slide 17: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
The system has a cache that is 8192 bytes.
How many lines does the cache have?
(8192 bytes/cache) / (512 bytes/line) = 16 lines/cache
If the cache is direct mapped, into how many possible lines can a block be placed?

## Slide 18: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
The system has a cache that is 8192 bytes.
How many lines does the cache have?
(8192 bytes/cache) / (512 bytes/line) = 16 lines/cache
If the cache is direct mapped, into how many possible lines can a block be placed?
1 – each block maps to one line in the cache

## Slide 19: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
The system has a cache that is 8192 bytes.
How many lines does the cache have?
(8192 bytes/cache) / (512 bytes/line) = 16 lines/cache
If the cache is direct mapped, into how many possible lines can a block be placed?
1 – each block maps to one line in the cache
How many bits are in the line field and the tag field?

## Slide 20: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
The system has a cache that is 8192 bytes.
How many lines does the cache have?
(8192 bytes/cache) / (512 bytes/line) = 16 lines/cache
If the cache is direct mapped, into how many possible lines can a block be placed?
1 – each block maps to one line in the cache
How many bits are in the line field and the tag field?
16 lines, so log(16) = 4 bits in the line field (4 bits are needed to count to 16)
16-9-4 = 3 bits in the tag field

## Slide 21: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
The system has a cache that is 8192 bytes.
How many lines does the cache have?
(8192 bytes/cache) / (512 bytes/line) = 16 lines/cache
If the cache is 2-way set associative, into how many possible lines can a block be placed?

## Slide 22: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
The system has a cache that is 8192 bytes.
How many lines does the cache have?
(8192 bytes/cache) / (512 bytes/line) = 16 lines/cache
If the cache is 2-way set associative, into how many possible lines can a block be placed?
2 – a block will map to a set, and that set has two lines

## Slide 23: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
The system has a cache that is 8192 bytes.
How many lines does the cache have?
(8192 bytes/cache) / (512 bytes/line) = 16 lines/cache
If the cache is 2-way set associative, into how many possible lines can a block be placed?
2 – a block will map to a set, and that set has two lines
How many bits are in the set and tag fields?

## Slide 24: Example Problem 4
A system has a main memory of 65,536 bytes and is split into blocks of 512 bytes.
The system has a cache that is 8192 bytes.
How many lines does the cache have?
(8192 bytes/cache) / (512 bytes/line) = 16 lines/cache
If the cache is 2-way set associative, into how many possible lines can a block be placed?
2 – a block will map to a set, and that set has two lines
How many bits are in the set and tag fields?
(16 lines/cache) / (2 lines/set) = 8 sets/cache
log(8) = 3, set field is 3 bits
Tag = 16-9-3 = 4 bits

## Slide 25
A system has a main memory with 232 bytes has a block size of 16 bytes and a cache size of 212 bytes.
If address 0x123123FF is requested, and the cache is fully associative, what is the tag and what is the offset?
Where will the system look in the cache for the tag? How may possible places could this byte be if it is in the cache?

## Slide 26
A system has a main memory with 232 bytes has a block size of 16 bytes and a cache size of 212 bytes.
If address 0x123123FF is requested, and the cache is fully associative, what is the tag and what is the offset?
Where will the system look in the cache for the tag? How may possible places could this byte be if it is in the cache?
Offset field = log(16) = 4 bits
Address = 0001 0010 0011 0001 0010 0011 1111 1111
Tag = 0001001000110001001000111111 Offset = 1111
Number of lines = (212 bytes/cache) / (24 bytes/line) = 28 lines/cache
The system will look in every line of the cache, 28 possible places.

## Slide 27
A system has a main memory with 232 bytes has a block size of 16 bytes and a cache size of 212 bytes.
If address 0x123123FF is requested, and the cache is direct mapped, what is the tag, line and offset?
Where will the system look in the cache for the tag? How may possible places could this byte be if it is in the cache?

## Slide 28
A system has a main memory with 232 bytes has a block size of 16 bytes and a cache size of 212 bytes.
If address 0x123123FF is requested, and the cache is direct mapped, what is the tag, line and offset?
Where will the system look in the cache for the tag? How may possible places could this byte be if it is in the cache?
Offset field = log(16) = 4 bits
Number of lines = (212 bytes/cache) / (24 bytes/line) = 28 lines/cache
Line field = log(28) = 8 bits
Tag field = 32 – 8 – 4 = 20 bits
Address = 0001 0010 0011 0001 0010 0011 1111 1111
00010010001100010010 00111111 1111
Tag = 00010010001100010010
Line = 00111111
Offset = 1111
There is one possible place where this byte could be, and that is at line 00111111. The system will look at that line to see if the tag matches

## Slide 29
A system has a main memory with 232 bytes has a block size of 16 bytes and a cache size of 212 bytes.
If address 0x123123FF is requested, and the cache is 4-way set associative, what is the tag, line and offset?
Where will the system look in the cache for the tag? How may possible places could this byte be if it is in the cache?

## Slide 30
A system has a main memory with 232 bytes has a block size of 16 bytes and a cache size of 212 bytes.
If address 0x123123FF is requested, and the cache is 4-way set associative, what is the tag, line and offset?
Where will the system look in the cache for the tag? How may possible places could this byte be if it is in the cache?
Offset field = log(16) = 4 bits
Number of sets = (212 bytes/cache) / ((24 bytes/line)*(4 lines/set)) = 26 sets/cache
Set field = log(26) = 6 bits
Tag field = 32 – 6 – 4 = 22 bits
Address = 0001 0010 0011 0001 0010 0011 1111 1111
0001001000110001001000 111111 1111
Tag = 0001001000110001001000
Set = 111111
Offset = 1111
The system will look at set 111111. There are four lines there, each with a tag. It will look at those four tags and see if one of them is a match.