## Slide 1: Cache Sample Problems
10 November
CDA 3101

## Slide 2: What is on the examlet?
Average memory access time
  Look aside
  Look through
Cache Designs – identify fields in addresses
  Direct mapped
  Fully associative
  Set associative

## Slide 3: Lookaside Cache
Accesses to cache and to main memory occur in parallel
Main memory access is cancelled if hit in cache occurs
Tends to lower average memory access time
Increases CPU to memory traffic
Average memory access time (AMAT) = hit ratio*TC + (1-hit ratio)*TM

## Slide 4: Look Through Cache
First level cache is checked first
Next level is only checked if miss occurs
Tends to increase average memory access time
Avoids unneeded CPU-to-memory traffic
AMAT = hit ratio*TC + (1-hit ratio)*(TC+TM) = TC + (1-hit ratio)*TM

## Slide 5: Example Problem
Consider a system with a main memory access time of 40 ns supported by an L1 cache having a 5 ns access time and a hit rate of 90% and an L2 cache having a 10 ns access time and a hit rate of 80%
What is the average memory access time for a look aside cache?
What is the average memory access time for a look through cache?

## Slide 6: Example Problem: Step 1
Consider a system with a main memory access time of 40 ns supported by an L1 cache having a 5 ns access time and a hit rate of 90% and an L2 cache having a 10 ns access time and a hit rate of 80%
What is the average memory access time for a look aside cache?
0.9(5) + 0.1(0.8(10) + 0.2(40)) = 4.5+0.1(8+8) = 4.5+1.6 = 6.1 ns
What is the average memory access time for a look through cache?

## Slide 7: Example Problem: Step 2
Consider a system with a main memory access time of 40 ns supported by an L1 cache having a 5 ns access time and a hit rate of 90% and an L2 cache having a 10 ns access time and a hit rate of 80%
What is the average memory access time for a look aside cache?
0.9(5) + 0.1(0.8(10) + 0.2(40)) = 4.5+0.1(8+8) = 4.5+1.6 = 6.1 ns
What is the average memory access time for a look through cache?
0.9(5) + 0.1(0.8(5+10) + 0.2(40+10+5)) = 4.5+0.1(12+11) = 4.5+2.3 = 6.8 ns
5 + 0.1(10 + 0.2(40)) = 5 + 0.1(10+8) = 5+1.8 = 6.8 ns

## Slide 8: Cache Organization
A block is the basic unit of transfer between memory and cache
A miss results in copying the entire block to cache
  Takes advantage of spatial locality
Cache is organized into some number of sets
Associativity is the number of blocks per set
  N-way associative means there are N blocks per set

## Slide 9: Fully Associative
Mapping is based on dividing address into two fields
  Tag field and offset
A separate tag is stored for each cache line
If a stored tag matches the tag field in the address and the line is valid, there is a hit.
Example: 14-bit addresses and a cache containing 16 lines. Each line is 8 bytes in size. Offset field width in bits = log2(line size)

## Slide 10: Fully Associative

## Slide 11: Direct Mapped

## Slide 12: Direct Mapped
Multiple addresses with same line number cause conflicts
  Cache line can hold only one candidate block
  Other vacant lines may be unused
  Causes increased miss ratio
Can hurt performance
  0 hit ratio if alternating between conflicting addresses

## Slide 13: Set Associative
2-way set associative cache (2 lines per set)
214 bytes of main memory
Cache with 128 bytes, and 8 bytes/line
(128 bytes/cache)/(8 bytes/line * 2 lines/set) =
128/16 = 8 sets/cache
Set field = log(8) = 3 bits
Offset field = log(8) = 3 bits
Address 0x12CF = 01 0010 1100 1111 =
01001011 001 111
Tag set offset

## Slide 14: Example Problem 2
A system has a main memory with 232 bytes has a block size of 16 bytes and a cache size of 212 bytes.
If address 0x123123FF is requested, and the cache is fully associative, what is the tag and what is the offset?
Where will the system look in the cache for the tag? How may possible places could this byte be if it is in the cache?

## Slide 15: Example Problem 2 Answer
A system has a main memory with 232 bytes has a block size of 16 bytes and a cache size of 212 bytes.
If address 0x123123FF is requested, and the cache is fully associative, what is the tag and what is the offset?
Where will the system look in the cache for the tag? How may possible places could this byte be if it is in the cache?
Offset field = log(16) = 4 bits
Address = 0001 0010 0011 0001 0010 0011 1111 1111
Tag = 0001001000110001001000111111 Offset = 1111
Number of lines = (212 bytes/cache) / (24 bytes/line) = 28 lines/cache
The system will look in every line of the cache, 28 possible places.

## Slide 16: Example Problem 3
A system has a main memory with 232 bytes has a block size of 16 bytes and a cache size of 212 bytes.
If address 0x123123FF is requested, and the cache is direct mapped, what is the tag, line and offset?
Where will the system look in the cache for the tag? How may possible places could this byte be if it is in the cache?

## Slide 17: Example Problem 3 Answer
A system has a main memory with 232 bytes has a block size of 16 bytes and a cache size of 212 bytes.
If address 0x123123FF is requested, and the cache is direct mapped, what is the tag, line and offset?
Where will the system look in the cache for the tag? How may possible places could this byte be if it is in the cache?
Offset field = log(16) = 4 bits
Number of lines = (212 bytes/cache) / (24 bytes/line) = 28 lines/cache
Line field = log(28) = 8 bits
Tag field = 32 – 8 – 4 = 20 bits
Address = 0001 0010 0011 0001 0010 0011 1111 1111
00010010001100010010 00111111 1111
Tag = 00010010001100010010
Line = 00111111
Offset = 1111
There is one possible place where this byte could be, and that is at line 00111111. The system will look at that line to see if the tag matches

## Slide 18: Example Problem 3 Answer Part 2
A system has a main memory with 232 bytes has a block size of 16 bytes and a cache size of 212 bytes.
If address 0x123123FF is requested, and the cache is 4-way set associative, what is the tag, line and offset?
Where will the system look in the cache for the tag? How may possible places could this byte be if it is in the cache?
Offset field = log(16) = 4 bits
Number of sets = (212 bytes/cache) / ((24 bytes/line)*(4 lines/set)) = 26 sets/cache
Set field = log(26) = 6 bits
Tag field = 32 – 6 – 4 = 22 bits
Address = 0001 0010 0011 0001 0010 0011 1111 1111
0001001000110001001000 111111 1111
Tag = 0001001000110001001000
Set = 111111
Offset = 1111
The system will look at set 111111. There are four lines there, each with a tag. It will look at those four tags and see if one of them is a match.