## Slide 1: Cache Sample Problems
CDA 3101

## Slide 2: Memory Hierarchy
Data Movement Occurs Across Memory Hierarchy
Access Latencies Differ Widely
  Register < L1 Cache < L2 Cache < Main Memory < Disk < Archival
Memory Performance Can be Maximized
  Maximize Data Transfers in Fast Memory (e.g. Registers <-> Cache)
  Minimize Data Transfers in Slow Memory (e.g. Registers <-> Main Memory)
Place data most likely to be accessed (needed in a register) in fast memory

## Slide 3: Sample Configuration of Cache Memory

## Slide 4: Cache Memory
Blocks containing a desired item are loaded into cache
  Blocks may contain hundreds of bytes
  Takes advantage of spatial locality
Blocks are copied from main memory into L2 and L1 cache
L1 contains a subset of information in L2
Cache line holds a block read from main memory
  Blocks and lines are the same size
  Blocks are in main memory, lines are in cache

## Slide 5: Lookaside Cache
Accesses to cache and to main memory occur in parallel
Main memory access is cancelled if hit in cache occurs
Tends to lower average memory access time
Increases CPU to memory traffic
Average memory access time (AMAT) = hit ratio*TC + (1-hit ratio)*TM

## Slide 6: Look Through Cache
First level cache is checked first
Next level is only checked if miss occurs
Tends to increase average memory access time
Avoids unneeded CPU-to-memory traffic
AMAT = hit ratio*TC + (1-hit ratio)*(TC+TM) = TC + (1-hit ratio)*TM

## Slide 7: Example Problem 1
Consider a system with a main memory access time of 50 ns supported by a cache having a 8 ns access time and a hit rate of 95%.
What is the average memory access time for a look aside cache?
What is the average memory access time for a look through cache?

## Slide 8: Example Problem 1 Step 1
Consider a system with a main memory access time of 50 ns supported by a cache having a 8 ns access time and a hit rate of 95%.
What is the average memory access time for a look aside cache?
Hit ratio = 0.95
AMAT = 0.95*8 + 0.05*50 = 10.1 ns
What is the average memory access time for a look through cache?

## Slide 9: Example Problem 1 Step 2
Consider a system with a main memory access time of 50 ns supported by a cache having a 8 ns access time and a hit rate of 95%.
What is the average memory access time for a look aside cache?
Hit ratio = 0.95
AMAT = 0.95*8 + 0.05*50 = 10.1 ns
What is the average memory access time for a look through cache?
AMAT = 0.95*8 + 0.05(8 + 50) = 8 + 0.05*50 = 10.5 ns

## Slide 10: Example Problem 2
Consider a system with a main memory access time of 50 ns supported by an L1 cache having a 8 ns access time and a hit rate of 95% and an L2 cache having a 15 ns access time and a hit rate of 90%
What is the average memory access time for a look aside cache?
What is the average memory access time for a look through cache?

## Slide 11: Example Problem 2 Step 1
Consider a system with a main memory access time of 50 ns supported by an L1 cache having a 8 ns access time and a hit rate of 95% and an L2 cache having a 15 ns access time and a hit rate of 90%
What is the average memory access time for a look aside cache?
8*0.95 + 0.05(15*0.9 + 50*0.1) = 8.525 ns
What is the average memory access time for a look through cache?

## Slide 12: Example Problem 2 Step 2
Consider a system with a main memory access time of 50 ns supported by an L1 cache having a 8 ns access time and a hit rate of 95% and an L2 cache having a 15 ns access time and a hit rate of 90%
What is the average memory access time for a look aside cache?
8*0.95 + 0.05(15*0.9 + 50*0.1) = 8.525 ns
What is the average memory access time for a look through cache?
8 + 0.05*(15 + 50*0.1) = 9 ns

## Slide 13: Sources of Misses
Compulsory Misses
  Also called “cold start” misses
  Unavoidable due to initially empty cache
Capacity
  Due to limited size of cache
Conflict
  Due to different blocks mapping to the same cache line

## Slide 14: Cache Organization
Main memory is split into blocks - blocks will be loaded into cache
Addresses of items map to blocks
Block number = address/block size
Number of bits in offset = log2 block size
Example: for 256-byte blocks, the address 0x0400ACE8 falls within block: 0x400ACE8/256=0x00400AC
  Offset width = log2 256 = 8 bits

## Slide 15: Example Problem 3
Main memory size = 16 bytes = 24 bytes
Address is log(16) = 4 bits
Block size = 4 bytes = 22 bytes
Width of offset field is log(4) = 2 bits
Block number = 4-2 = 2 bits
Memory Address | Block | Offset
0000 | 00 | 00
0001 | 00 | 01
0010 | 00 | 10
0011 | 00 | 11
0100 | 01 | 00
0101 | 01 | 01
0110 | 01 | 10
0111 | 01 | 11
1000 | 10 | 00
1001 | 10 | 01
1010 | 10 | 10
1011 | 10 | 11
1100 | 11 | 00
1101 | 11 | 01
1110 | 11 | 10
1111 | 11 | 11

## Slide 16: Example Problem 3 Step 1
Main memory size = 16 bytes = 24 bytes
Address is log(16) = 4 bits
Block size = 4 bytes = 22 bytes
Width of offset field is log(4) = 2 bits
Block number = 4-2 = 2 bits
Example: memory address 910 = 10012
Block number = floor(9/4) = 210 = 102
Or, just take the first two bits = 10
Offset = 01
How far in the block to we have to go to find the item requested?
Memory Address | Block | Offset
0000 | 00 | 00
0001 | 00 | 01
0010 | 00 | 10
0011 | 00 | 11
0100 | 01 | 00
0101 | 01 | 01
0110 | 01 | 10
0111 | 01 | 11
1000 | 10 | 00
1001 | 10 | 01
1010 | 10 | 10
1011 | 10 | 11
1100 | 11 | 00
1101 | 11 | 01
1110 | 11 | 10
1111 | 11 | 11

## Slide 17: Example Problem 4
Main memory of 65,536 bytes is split into blocks of 512 bytes.
How many bits wide is the memory address?
How many bits wide is the offset field?
How many bits describe the block?

## Slide 18: Example Problem 4 Answer
Main memory of 65,536 bytes is split into blocks of 512 bytes.
How many bits wide is the memory address?
log(65536) = 16
How many bits wide is the offset field?
log(512) = 9
How many bits describe the block?
16 - 9 = 7 bits

## Slide 19: Cache Organization
Cache can hold some number of blocks
  The blocks within the cache are called lines
  Each line is the same size as a memory block
  A line can hold one of a collection of blocks
  Mapping determines which line contains which block
Number of lines is much smaller than number of blocks
  Main memory size / block size = number of blocks
  Cache size / block size = number of lines
  If cache size = 213 bytes and block size is 256 bytes, number of lines = 213 B/ 28 B = 25 = 32 lines

## Slide 20: Example Problem 5
A system has a main memory of 232 bytes and a block size of 1024 bytes. It has a cache with 16,834 bytes.
How many bits are in the memory address?
How many blocks are in main memory?
What is the size of the offset field?
How many lines are in the cache?

## Slide 21: Example Problem 5 Answer
A system has a main memory of 232 bytes and a block size of 1024 bytes. It has a cache with 16,834 bytes.
How many bits are in the memory address?
log(232) = 32
How many blocks are in main memory?
1024 = 210
232 bytes / (1024 bytes/block) = 232 / 210 = 222 blocks
How many bits are in the offset field?
Log(210) = 10
How many lines are in the cache?
16,834 = 214
214 bytes/cache / 210 bytes/line = 24 lines/cache

## Slide 22: Fully Associative
Any memory block can go into any empty cache line
All lines are checked to detect cache hits or misses
Requires hardware to compare all lines in parallel
  A valid bit for each line is set if the line is occupied
  Block loaded into vacant cache line if miss occurs
  If no line is vacant a replacement must occur

## Slide 23: Fully Associative
Mapping is based on dividing address into two fields
  Tag field and offset
A separate tag is stored for each cache line
If a stored tag matches the tag field in the address and the line is valid, there is a hit.
Example: 14-bit addresses and a cache containing 16 lines. Each line is 8 bytes in size. Offset field width in bits = log2(line size)

## Slide 24: Fully Associative

## Slide 25: Example Problem 6
A system with 232 bytes of main memory has a fully associative cache with 210 bytes and a line size of 24 bytes.
How many bits are in the address?
How many bits are in the offset field?
How many bits are in the tag (or block) field?
How many lines are in the cache?

## Slide 26: Example Problem 6 Answer
A system with 232 bytes of main memory has a fully associative cache with 210 bytes and a line size of 24 bytes.
How many bits are in the address? log(232) = 32
How many bits are in the offset field? log(24 ) = 4
How many bits are in the tag (or block) field? 32 – 4 = 28
How many lines are in the cache? (210 bytes/cache) / (24 bytes/line) = 26 lines/cache

## Slide 27: Example Problem 6 Step 2
A system with 232 bytes of main memory has a fully associative cache with 210 bytes and a line size of 24 bytes.
How many bits are in the address? 32
How many bits are in the offset field? 4
How many bits are in the tag (or block) field? 32 – 4 = 28
How many lines are in the cache? (210 bytes/cache) / (24 bytes/line) = 26 lines/cache
A request is made for the byte at address 0x12345678. What is the tag?

## Slide 28: Example Problem 6 Step 2 Answer
A system with 232 bytes of main memory has a fully associative cache with 210 bytes and a line size of 24 bytes.
How many bits are in the address? 32
How many bits are in the offset field? 4
How many bits are in the tag (or block) field? 32 – 4 = 28
How many lines are in the cache? (210 bytes/cache) / (24 bytes/line) = 26 lines/cache
A request is made for the byte at address 0x12345678. What is the tag?
0x1234567 (all but lowest 4 bits)

## Slide 29: Example Problem 7
A system with 216 bytes in the main memory. It has a fully associative cache with 25 bytes and a line size of 22 bytes.
The cache state is currently as below.
 | Line byte 1 | Line byte 2 | Line byte 2 | Line byte 4 | Line byte 3 |  | Line byte 4 | 
Tag | Offset | Data | Offset | Data | Offset | Data | Offset | data
11010101110010 | 00 | 10101010 | 01 | 00010010 | 10 | 00111110 | 11 | 00100001
10111111000000 | 00 | 10010011 | 01 | 11110000 | 10 | 01010100 | 11 | 10101011
00000000000001 | 00 | 11111111 | 01 | 00000000 | 10 | 11111100 | 11 | 00000011
01111110100110 | 00 | 10101010 | 01 | 01010101 | 10 | 00000000 | 11 | 00000000
There is a request for address 0x0007. Is it a hit or miss?
If it is a hit, what is returned? If it is a miss, what is the state of the cache after the data is obtained from main memory?

## Slide 30: Example Problem 7 Answer
A system with 216 bytes in the main memory. It has a fully associative cache with 25 bytes and a line size of 22 bytes.
The cache state is currently as below.
 | Line byte 1 | Line byte 2 | Line byte 2 | Line byte 4 | Line byte 3 |  | Line byte 4 | 
Tag | Offset | Data | Offset | Data | Offset | Data | Offset | data
11010101110010 | 00 | 10101010 | 01 | 00010010 | 10 | 00111110 | 11 | 00100001
10111111000000 | 00 | 10010011 | 01 | 11110000 | 10 | 01010100 | 11 | 10101011
00000000000001 | 00 | 11111111 | 01 | 00000000 | 10 | 11111100 | 11 | 00000011
01111110100110 | 00 | 10101010 | 01 | 01010101 | 10 | 00000000 | 11 | 00000000
There is a request for address 0x0007. Is it a hit or miss? Address is 16 bites, Offset = log(22) = 2 bits, tag = 14 bits
Address = 0000 0000 0000 0111 tag = 00000000000001 that is a hit, offset = 11, value returned = 00000011

## Slide 31: Example Problem 7 Step 2
A system with 216 bytes in the main memory. It has a fully associative cache with 25 bytes and a line size of 22 bytes.
The cache state is currently as below.
 | Line byte 1 | Line byte 2 | Line byte 2 | Line byte 4 | Line byte 3 |  | Line byte 4 | 
Tag | Offset | Data | Offset | Data | Offset | Data | Offset | data
11010101110010 | 00 | 10101010 | 01 | 00010010 | 10 | 00111110 | 11 | 00100001
10111111000000 | 00 | 10010011 | 01 | 11110000 | 10 | 01010100 | 11 | 10101011
00000000000001 | 00 | 11111111 | 01 | 00000000 | 10 | 11111100 | 11 | 00000011
01111110100110 | 00 | 10101010 | 01 | 01010101 | 10 | 00000000 | 11 | 00000000
There is a request for address 0xBB35. Is it a hit or miss?
If it is a hit, what is returned? If it is a miss, what is the state of the cache after the data is obtained from main memory?

## Slide 32: Example Problem 7 Step 2 Answer
A system with 216 bytes in the main memory. It has a fully associative cache with 25 bytes and a line size of 22 bytes.
The cache state is currently as below.
 | Line byte 1 | Line byte 2 | Line byte 2 | Line byte 4 | Line byte 3 |  | Line byte 4 | 
Tag | Offset | Data | Offset | Data | Offset | Data | Offset | data
11010101110010 | 00 | 10101010 | 01 | 00010010 | 10 | 00111110 | 11 | 00100001
10111111000000 | 00 | 10010011 | 01 | 11110000 | 10 | 01010100 | 11 | 10101011
00000000000001 | 00 | 11111111 | 01 | 00000000 | 10 | 11111100 | 11 | 00000011
01111110100110 | 00 | 10101010 | 01 | 01010101 | 10 | 00000000 | 11 | 00000000
There is a request for address 0xBB35. Is it a hit or miss?
1011 1011 0011 0101, tag = 10111011001101 a miss
This block is fetched from main memory and placed in the next line of the cache

## Slide 33: Example Problem 7 Step 3
A system with 216 bytes in the main memory. It has a fully associative cache with 25 bytes and a line size of 22 bytes.
The cache state is currently as below.
 | Line byte 1 | Line byte 2 | Line byte 2 | Line byte 4 | Line byte 3 |  | Line byte 4 | 
Tag | Offset | Data | Offset | Data | Offset | Data | Offset | data
11010101110010 | 00 | 10101010 | 01 | 00010010 | 10 | 00111110 | 11 | 00100001
10111111000000 | 00 | 10010011 | 01 | 11110000 | 10 | 01010100 | 11 | 10101011
00000000000001 | 00 | 11111111 | 01 | 00000000 | 10 | 11111100 | 11 | 00000011
01111110100110 | 00 | 10101010 | 01 | 01010101 | 10 | 00000000 | 11 | 00000000
10111011001101 | 00 | ???????? | 01 | ???????? | 10 | ????????? | 11 | ?????????
There is a request for address 0xBB35. Is it a hit or miss?
1011 1011 0011 0101, tag = 10111011001101 a miss
This block is fetched from main memory and placed in the next line of the cache

## Slide 34: Direct Mapped
Fully Associative is one extreme
  A separate comparator is required for every cache line
Direct mapped is the other extreme
  Only one comparator is needed for the entire cache
With a direct mapped cache with N lines:
  Block B of memory maps to line L = B mod N
  B is the block number, not the address
Example: direct mapped cache with 10 lines, Line 6 may hold block 6 or 16 or 26 or 36 …

## Slide 35: Direct Mapped
Direct Mapped

## Slide 36: Direct Mapped
Direct Mapped

## Slide 37: Direct Mapped
Main memory with 24 bytes, and blocks of 22 bytes.
Cache with 23 bytes, (23 bytes/cache) / (22 bytes/line) = 2 lines/cache
Offset field = log(22) = 2 bits, Line field = log(2) = 1 bit, Tag field = 4-2-1 = 1
Direct Mapped

## Slide 38: Direct Mapped
Multiple addresses with same line number cause conflicts
  Cache line can hold only one candidate block
  Other vacant lines may be unused
  Causes increased miss ratio
Can hurt performance
  0 hit ratio if alternating between conflicting addresses

## Slide 39: Example Problem 8
A system has a main memory of 232 bytes. It has a direct mapped cache that is 212 bytes and a block size of 16 bytes.
How many bits are in the address?
How many lines are in the cache?
How many bits are in the offset?
How many bits are in the line field?
A program wants to access the data at address 0xABCD0123.
At what line number in the cache would it be located?
What is the tag?
Example Problem 8

## Slide 40: Example Problem 8 Answer
A system has a main memory of 232 bytes. It has a direct mapped cache that is 212 bytes and a block size of 16 bytes.
How many bits are in the address? 32
How many lines are in the cache? 212 bytes/cache / 24 bytes/line = 28 lines/cache
How many bits are in the offset? log(24) = 4
How many bits are in the line field? log(28) = 8
A program wants to access the data at address 0xABCD0123.
At what line number in the cache would it be located?
What is the tag?
Example Problem 8 Answer

## Slide 41: Example Problem 8 Step 2
A system has a main memory of 232 bytes. It has a direct mapped cache that is 212 bytes and a block size of 16 bytes.
How many bits are in the address? 32
How many lines are in the cache? 212 bytes/cache / 24 bytes/line = 28 lines/cache
How many bits are in the offset? log(24) = 4
How many bits are in the line field? log(28) = 8
A program wants to access the data at address 0xABCD0123.
1010 1011 1100 1101 0000 0001 0010 0011
10101011110011010000 00010010 0011
At what line number in the cache would it be located?
00010010 = line 18
What is the tag?
10101011110011010000
Example Problem 8 Step 2

## Slide 42: Example Problem 9 Step 1
Example Problem 9 Step 1
A system has 24 bytes of main memory and a direct mapped cache with 8 bytes. A line is 2 bytes. The main memory is as shown below.
Address = 4 bits
Offset field = log(2) = 1 bit
(8 bytes/cache) / (2 bytes/line) = 4 lines/cache
Line field = log(4) = 2 bits
Tag field = 4 – 1 – 2 = 1 bit
Line | Tag | Data
00 | 1 | 0xACD7
01 | 0 | 0x1243
10 | 0 | 0xA398
11 | 1 | 0x72AC
Block | Data
000 | 0xAABB
001 | 0x1243
010 | 0xA398
011 | 0x98AB
100 | 0xACD7
101 | 0x9900
110 | 0x0099
111 | 0x72AC
The cache state is as shown in the table. The data at address 0xA is requested. Is this a hit or a miss? What data is returned?

## Slide 43: Example Problem 9 Step 2
Example Problem 9 Step 2
A system has 24 bytes of main memory and a direct mapped cache with 8 bytes. A line is 2 bytes. The main memory is as shown below.
Address = 4 bits
Offset field = log(2) = 1 bit
(8 bytes/cache) / (2 bytes/line) = 4 lines/cache
Line field = log(4) = 2 bits
Tag field = 4 – 1 – 2 = 1 bit
Line | Tag | Data
00 | 1 | 0xACD7
01 | 0 | 0x1243
10 | 0 | 0xA398
11 | 1 | 0x72AC
Block | Data
000 | 0xAABB
001 | 0x1243
010 | 0xA398
011 | 0x98AB
100 | 0xACD7
101 | 0x9900
110 | 0x0099
111 | 0x72AC
The cache state is as shown in the table. The data at address 0xA is requested. Is this a hit or a miss?
0xA = 1010 Tag = 1, Line = 01, this is a miss. What data is returned?

## Slide 44: Example Problem 9 Step 3
Example Problem 9 Step 3
A system has 24 bytes of main memory and a direct mapped cache with 8 bytes. A line is 2 bytes. The main memory is as shown below.
Address = 4 bits
Offset field = log(2) = 1 bit
(8 bytes/cache) / (2 bytes/line) = 4 lines/cache
Line field = log(4) = 2 bits
Tag field = 4 – 1 – 2 = 1 bit
Line | Tag | Data
00 | 1 | 0xACD7
01 | 1 | 0x9900
10 | 0 | 0xA398
11 | 1 | 0x72AC
Block | Data
000 | 0xAABB
001 | 0x1243
010 | 0xA398
011 | 0x98AB
100 | 0xACD7
101 | 0x9900
110 | 0x0099
111 | 0x72AC
The cache state is as shown in the table. The data at address 0xA is requested. Is this a hit or a miss?
0xA = 1010 Tag = 1, Line = 01, this is a miss. What data is returned? Offset is 0, so data returned 0x99. The block is placed in line 01.

## Slide 45: Example Problem 9 Step 4
Example Problem 9 Step 4
A system has 24 bytes of main memory and a direct mapped cache with 8 bytes. A line is 2 bytes. The main memory is as shown below.
Address = 4 bits
Offset field = log(2) = 1 bit
(8 bytes/cache) / (2 bytes/line) = 4 lines/cache
Line field = log(4) = 2 bits
Tag field = 4 – 1 – 2 = 1 bit
Line | Tag | Data
00 | 1 | 0xACD7
01 | 1 | 0x9900
10 | 0 | 0xA398
11 | 1 | 0x72AC
Block | Data
000 | 0xAABB
001 | 0x1243
010 | 0xA398
011 | 0x98AB
100 | 0xACD7
101 | 0x9900
110 | 0x0099
111 | 0x72AC
The cache state is as shown in the table. The data at address 0xF is requested. Is this a hit or a miss? What data is returned?

## Slide 46: Example Problem 9 Step 5
Example Problem 9 Step 5
A system has 24 bytes of main memory and a direct mapped cache with 8 bytes. A line is 2 bytes. The main memory is as shown below.
Address = 4 bits
Offset field = log(2) = 1 bit
(8 bytes/cache) / (2 bytes/line) = 4 lines/cache
Line field = log(4) = 2 bits
Tag field = 4 – 1 – 2 = 1 bit
Line | Tag | Data
00 | 1 | 0xACD7
01 | 1 | 0x9900
10 | 0 | 0xA398
11 | 1 | 0x72AC
Block | Data
000 | 0xAABB
001 | 0x1243
010 | 0xA398
011 | 0x98AB
100 | 0xACD7
101 | 0x9900
110 | 0x0099
111 | 0x72AC
The cache state is as shown in the table. The data at address 0xF is requested. Is this a hit or a miss? 0xF = 1111, tag = 1, line = 11, this is a hit What data is returned? The offset is 1, so the data returned is 0xAC

## Slide 47: Example Problem 9 Step 6
Example Problem 9 Step 6
A system has 24 bytes of main memory and a direct mapped cache with 8 bytes. A line is 2 bytes. The main memory is as shown below.
Address = 4 bits
Offset field = log(2) = 1 bit
(8 bytes/cache) / (2 bytes/line) = 4 lines/cache
Line field = log(4) = 2 bits
Tag field = 4 – 1 – 2 = 1 bit
Line | Tag | Data
00 | 1 | 0xACD7
01 | 1 | 0x9900
10 | 0 | 0xA398
11 | 1 | 0x72AC
Block | Data
000 | 0xAABB
001 | 0x1243
010 | 0xA398
011 | 0x98AB
100 | 0xACD7
101 | 0x9900
110 | 0x0099
111 | 0x72AC
The cache state is as shown in the table. The data at address 0x3 is requested. Is this a hit or a miss? What data is returned?

## Slide 48: Example Problem 9 Step 7
Example Problem 9 Step 7
A system has 24 bytes of main memory and a direct mapped cache with 8 bytes. A line is 2 bytes. The main memory is as shown below.
Address = 4 bits
Offset field = log(2) = 1 bit
(8 bytes/cache) / (2 bytes/line) = 4 lines/cache
Line field = log(4) = 2 bits
Tag field = 4 – 1 – 2 = 1 bit
Line | Tag | Data
00 | 1 | 0xACD7
01 | 1 | 0x9900
10 | 0 | 0xA398
11 | 1 | 0x72AC
The cache state is as shown in the table. The data at address 0x3 is requested. 0x3 = 0011, tag =0, line=01, Is this a hit or a miss? This is a miss. What data is returned?
Block | Data
000 | 0xAABB
001 | 0x1243
010 | 0xA398
011 | 0x98AB
100 | 0xACD7
101 | 0x9900
110 | 0x0099
111 | 0x72AC

## Slide 49: Example Problem 9 Step 8
Example Problem 9 Step 8
A system has 24 bytes of main memory and a direct mapped cache with 8 bytes. A line is 2 bytes. The main memory is as shown below.
Address = 4 bits
Offset field = log(2) = 1 bit
(8 bytes/cache) / (2 bytes/line) = 4 lines/cache
Line field = log(4) = 2 bits
Tag field = 4 – 1 – 2 = 1 bit
Line | Tag | Data
00 | 1 | 0xACD7
01 | 0 | 0x1243
10 | 0 | 0xA398
11 | 1 | 0x72AC
Block | Data
000 | 0xAABB
001 | 0x1243
010 | 0xA398
011 | 0x98AB
100 | 0xACD7
101 | 0x9900
110 | 0x0099
111 | 0x72AC
The cache state is as shown in the table. The data at address 0x3 is requested. 0x3 = 0011, tag =0, line=01, Is this a hit or a miss? This is a miss. What data is returned? The offset is 1, so 0x43 is returned and block 001 is placed in the cache

## Slide 50: Set Associative
Lines are put into sets
A number of blocks can be mapped to and put in the same set
Reduces conflicts
Addresses are divided into three fields
  tag, set, offset
Set field determines set (group of lines) to which the memory block maps
Tag field identifies which line within the set contains the block (if it is there)
Offset field chooses the location within the line

## Slide 51: Set Associative
2-way set associative cache (2 lines per set)
214 bytes of main memory
Cache with 128 bytes, and 8 bytes/line
(128 bytes/cache)/(8 bytes/line * 2 lines/set) =
128/16 = 8 sets/cache
Set field = log(8) = 3 bits
Offset field = log(8) = 3 bits

## Slide 52: Set Associative
2-way set associative cache (2 lines per set)
214 bytes of main memory
Cache with 128 bytes, and 8 bytes/line
(128 bytes/cache)/(8 bytes/line * 2 lines/set) =
128/16 = 8 sets/cache
Set field = log(8) = 3 bits
Offset field = log(8) = 3 bits
Address 0x12CF = 01 0010 1100 1111 =
01001011 001 111
Tag set offset

## Slide 53: Set Associative

## Slide 54: Example Problem 10 Step 1
Example Problem 10 Step 1

## Slide 55: Example Problem 10 Step 2
Example Problem 10 Step 2

## Slide 56: Example Problem 10 Step 3
Example Problem 10 Step 3

## Slide 57: Example Problem 10 Step 4
Example Problem 10 Step 4

## Slide 58: Example Problem 10 Step 5
Example Problem 10 Step 5

## Slide 59: Example Problem 10 Step 6
Example Problem 10 Step 6

## Slide 60: Example Problem 11
Example Problem 11
A system has a main memory of 232 bytes with a 25 byte block size.
It has a 4-way set associative cache with 210 bytes.
How many bits are in the address?
What is the size of the offset field?
How many sets are there?
How many bits in the set field?
How many bits in the tag field?

## Slide 61: Example Problem 11 Answer
Example Problem 11 Answer
A system has a main memory of 232 bytes with a 25 byte block size.
It has a 4-way set associative cache with 210 bytes.
How many bits are in the address? 32 bits
What is the size of the offset field? log(25) = 5 bits
How many sets are there?
210 bytes/cache / (25 bytes/line * 4 lines/set) = 23 sets/cache
How many bits in the set field? log(23) = 3 bits
How many bits in the tag field? 32-3-5 = 24 bits

## Slide 62: Example Problem 12
Example Problem 12
A system has a main memory with 232 bytes has a block size of 8 bytes and a cache size of 210 bytes.
If address 0xABCDEEF0 is requested, and the cache is fully associative, what is the tag and what is the offset?
Where will the system look in the cache for the tag? How may possible places could this byte be if it is in the cache?

## Slide 63: Example Problem 12 Answer
Example Problem 12 Answer
A system has a main memory with 232 bytes has a block size of 8 bytes and a cache size of 210 bytes.
If address 0xABCDEEF0 is requested, and the cache is fully associative, what is the tag and what is the offset?
Where will the system look in the cache for the tag? How may possible places could this byte be if it is in the cache?
The address is 32 bits. The offset field is log(8) = 3 bits.
The tag is 32-3 = 29 bits
ABCDEF0 = 1010 1011 1100 1101 1110 1110 1111 0000
10101011110011011110111011110 is the tag
The system will look in every line of the cache for the tag.
The data could be in any line. There are 210 / 23 = 27 lines, so there are 27 possible places this byte could be. It will look at the tag at every line in the cache, and if there is a match, then it is a hit.

## Slide 64: Example Problem 13
Example Problem 13
A system has a main memory with 232 bytes has a block size of 8 bytes and a cache size of 210 bytes.
If address 0xABCDEEF0 is requested, and the cache is direct mapped, what is the tag, what is the line, and what is the offset?
Where will the system look in the cache for the tag? How may possible places could this byte be if it is in the cache?

## Slide 65: Example Problem 13 Answer
Example Problem 13 Answer
A system has a main memory with 232 bytes has a block size of 8 bytes and a cache size of 210 bytes.
If address 0xABCDEEF0 is requested, and the cache is direct mapped, what is the tag, what is the line, and what is the offset?
Where will the system look in the cache for the tag? How may possible places could this byte be if it is in the cache?
The offset is log(8) = 3 bits
The number of lines in the cache = (210 bytes/cache )/(8 bytes/line) = 27 lines / cache
The line field is log(27) = 7 bits
The tag field is 32 – 3- 7 = 22 bits
ABCDEF0 = 1010 1011 1100 1101 1110 1110 1111 0000
1010101111001101111011 1011110 000
Tag = 1010101111001101111011 line= 1011110 offset=000
The system will look in line 1011110 for the tag. There is one place it could be, at line 1011110. The system will look at line 1011110, and if the tag matches, it is a hit.

## Slide 66: Example Problem 14
Example Problem 14
A system has a main memory with 232 bytes has a block size of 8 bytes and a cache size of 210 bytes.
If address 0xABCDEEF0 is requested, and the cache is 4-way set associative, what is the tag, what is the line, and what is the offset?
Where will the system look in the cache for the tag? How may possible places could this byte be if it is in the cache?

## Slide 67: Example Problem 14 Answer
Example Problem 14 Answer
A system has a main memory with 232 bytes has a block size of 8 bytes and a cache size of 210 bytes.
If address 0xABCDEEF0 is requested, and the cache is 4-way set associative, what is the tag, what is the line, and what is the offset?
Where will the system look in the cache for the tag? How may possible places could this byte be if it is in the cache?
The offset is log(8) = 3 bits
The number of sets = (210 bytes/cache) / (8 bytes/line * 4 lines/set) = 25 sets/cache
There are log(25) = 5 bits in the set field
There are 32 – 3 – 5 = 24 bits in the tag field
ABCDEF0 = 1010 1011 1100 1101 1110 1110 1111 0000
101010111100110111101110 11110 000
Tag = 10101011110011011110 set= 11110 offset=000
The system will look in set 11110. There are four possible places that this byte could be. Set 11110 has four lines in it, it will look at the tag values of these four lines to see if there is a match. If there is, it is a hit.