## Slide 1: Cache Sample Problems
CDA 3101

## Slide 2: Memory Hierarchy
Data Movement Occurs Across Memory Hierarchy
Access Latencies Differ Widely
  Register < L1 Cache < L2 Cache < Main Memory < Disk < Archival
Memory Performance Can be Maximized
  Maximize Data Transfers in Fast Memory (e.g. Registers <-> Cache)
  Minimize Data Transfers in Slow Memory (e.g. Registers <-> Main Memory)
Place data most likely to be accessed (needed in a register) in fast memory

## Slide 3: Sample Configuration of Cache Memory

## Slide 4: Cache Memory
Blocks containing a desired item are loaded into cache
  Blocks may contain hundreds of bytes
  Takes advantage of spatial locality
Blocks are copied from main memory into L2 and L1 cache
L1 contains a subset of information in L2
Cache line holds a block read from main memory
  Blocks and lines are the same size
  Blocks are in main memory, lines are in cache

## Slide 5: Lookaside Cache
Accesses to cache and to main memory occur in parallel
Main memory access is cancelled if hit in cache occurs
Tends to lower average memory access time
Increases CPU to memory traffic
Average memory access time (AMAT) = hit ratio*TC + (1-hit ratio)*TM

## Slide 6: Look Through Cache
First level cache is checked first
Next level is only checked if miss occurs
Tends to increase average memory access time
Avoids unneeded CPU-to-memory traffic
AMAT = hit ratio*TC + (1-hit ratio)*(TC+TM) = TC + (1-hit ratio)*TM

## Slide 7: Example Problem 1
Consider a system with a main memory access time of 50 ns supported by a cache having a 8 ns access time and a hit rate of 95%.
What is the average memory access time for a look aside cache?
0.95*8 +0.05*50
What is the average memory access time for a look through cache?

## Slide 8: Example Problem 1 Step 1
Consider a system with a main memory access time of 50 ns supported by a cache having a 8 ns access time and a hit rate of 95%.
What is the average memory access time for a look aside cache?
Hit ratio = 0.95
AMAT = 0.95*8 + 0.05*50 = 10.1 ns
What is the average memory access time for a look through cache?
8 + 0.05*50 =

## Slide 9: Example Problem 1 Step 2
Consider a system with a main memory access time of 50 ns supported by a cache having a 8 ns access time and a hit rate of 95%.
What is the average memory access time for a look aside cache?
Hit ratio = 0.95
AMAT = 0.95*8 + 0.05*50 = 10.1 ns
What is the average memory access time for a look through cache?
AMAT = 0.95*8 + 0.05(8 + 50) = 8 + 0.05*50 = 10.5 ns

## Slide 10: Example Problem 2
Consider a system with a main memory access time of 50 ns supported by an L1 cache having a 8 ns access time and a hit rate of 95% and an L2 cache having a 15 ns access time and a hit rate of 90%
What is the average memory access time for a look aside cache?
0.95*8 + 0.05*(0.9*15 + 0.1*50)
What is the average memory access time for a look through cache?

## Slide 11: Example Problem 2 Step 1
Consider a system with a main memory access time of 50 ns supported by an L1 cache having a 8 ns access time and a hit rate of 95% and an L2 cache having a 15 ns access time and a hit rate of 90%
What is the average memory access time for a look aside cache?
8*0.95 + 0.05(15*0.9 + 50*0.1) = 8.525 ns
What is the average memory access time for a look through cache?
8 + 0.05*(15 + 0.1*50) =

## Slide 12: Example Problem 2 Step 2
Consider a system with a main memory access time of 50 ns supported by an L1 cache having a 8 ns access time and a hit rate of 95% and an L2 cache having a 15 ns access time and a hit rate of 90%
What is the average memory access time for a look aside cache?
8*0.95 + 0.05(15*0.9 + 50*0.1) = 8.525 ns
What is the average memory access time for a look through cache?
8 + 0.05*(15 + 50*0.1) = 9 ns

## Slide 13: Sources of Misses
Compulsory Misses
  Also called “cold start” misses
  Unavoidable due to initially empty cache
Capacity
  Due to limited size of cache
Conflict
  Due to different blocks mapping to the same cache line

## Slide 14: Cache Organization
Main memory is split into blocks - blocks will be loaded into cache
Addresses of items map to blocks
Block number = address/block size
Number of bits in offset = log2 block size
Example: for 256-byte blocks, the address 0x0400ACE8 falls within block: 0x400ACE8/256=0x00400AC
  Offset width = log2 256 = 8 bits

## Slide 15: Example Problem 3
Main memory size = 16 bytes = 24 bytes
Address is log(16) = 4 bits
Block size = 4 bytes = 22 bytes
Width of offset field is log(4) = 2 bits
Block number = 4-2 = 2 bits
Memory Address | Block | Offset
0000 | 00 | 00
0001 | 00 | 01
0010 | 00 | 10
0011 | 00 | 11
0100 | 01 | 00
0101 | 01 | 01
0110 | 01 | 10
0111 | 01 | 11
1000 | 10 | 00
1001 | 10 | 01
1010 | 10 | 10
1011 | 10 | 11
1100 | 11 | 00
1101 | 11 | 01
1110 | 11 | 10
1111 | 11 | 11

## Slide 16: Example Problem 3 Step 1
Main memory size = 16 bytes = 24 bytes
Address is log(16) = 4 bits
Block size = 4 bytes = 22 bytes
Width of offset field is log(4) = 2 bits
Block number = 4-2 = 2 bits
Example: memory address 910 = 10012
Block number = floor(9/4) = 210 = 102
Or, just take the first two bits = 10
Offset = 01
How far in the block to we have to go to find the item requested?
Memory Address | Block | Offset
0000 | 00 | 00
0001 | 00 | 01
0010 | 00 | 10
0011 | 00 | 11
0100 | 01 | 00
0101 | 01 | 01
0110 | 01 | 10
0111 | 01 | 11
1000 | 10 | 00
1001 | 10 | 01
1010 | 10 | 10
1011 | 10 | 11
1100 | 11 | 00
1101 | 11 | 01
1110 | 11 | 10
1111 | 11 | 11

## Slide 17: Example Problem 4
Main memory of 65,536 bytes is split into blocks of 512 bytes.
How many bits wide is the memory address?
How many bits wide is the offset field?
How many bits describe the block?

## Slide 18: Example Problem 4 Answer
Main memory of 65,536 bytes is split into blocks of 512 bytes.
How many bits wide is the memory address?
log(65536) = 16
How many bits wide is the offset field?
log(512) = 9
How many bits describe the block?
16 - 9 = 7 bits

## Slide 19: Cache Organization
Cache can hold some number of blocks
  The blocks within the cache are called lines
  Each line is the same size as a memory block
  A line can hold one of a collection of blocks
  Mapping determines which line contains which block
Number of lines is much smaller than number of blocks
  Main memory size / block size = number of blocks
  Cache size / block size = number of lines
  If cache size = 213 bytes and block size is 256 bytes, number of lines = 213 B/ 28 B = 25 = 32 lines

## Slide 20: Example Problem 5
A system has a main memory of 232 bytes and a block size of 1024 bytes. It has a cache with 16,834 bytes.
How many bits are in the memory address?
How many blocks are in main memory?
What is the size of the offset field?
How many lines are in the cache?

## Slide 21: Example Problem 5 Answer
A system has a main memory of 232 bytes and a block size of 1024 bytes. It has a cache with 16,834 bytes.
How many bits are in the memory address?
log(232) = 32
How many blocks are in main memory?
1024 = 210
232 bytes / (1024 bytes/block) = 232 / 210 = 222 blocks
How many bits are in the offset field?
log(210) = 10
How many lines are in the cache?
16,834 = 214
214 bytes/cache / 210 bytes/line = 24 lines/cache

## Slide 22: Fully Associative
Any memory block can go into any empty cache line
All lines are checked to detect cache hits or misses
Requires hardware to compare all lines in parallel
  A valid bit for each line is set if the line is occupied
  Block loaded into vacant cache line if miss occurs
  If no line is vacant a replacement must occur

## Slide 23: Fully Associative
Mapping is based on dividing address into two fields
  Tag field and offset
A separate tag is stored for each cache line
If a stored tag matches the tag field in the address and the line is valid, there is a hit.
Example: 14-bit addresses and a cache containing 16 lines. Each line is 8 bytes in size. Offset field width in bits = log2(line size)

## Slide 24: Fully Associative

## Slide 25: Example Problem 6
A system with 232 bytes of main memory has a fully associative cache with 210 bytes and a line size of 24 bytes.
How many bits are in the address?
How many bits are in the offset field?
How many bits are in the tag (or block) field?
How many lines are in the cache?

## Slide 26: Example Problem 6 Answer
A system with 232 bytes of main memory has a fully associative cache with 210 bytes and a line size of 24 bytes.
How many bits are in the address? log(232) = 32
How many bits are in the offset field? log(24 ) = 4
How many bits are in the tag (or block) field? 32 – 4 = 28
How many lines are in the cache? (210 bytes/cache) / (24 bytes/line) = 26 lines/cache

## Slide 27: Example Problem 6 Step 2
A system with 232 bytes of main memory has a fully associative cache with 210 bytes and a line size of 24 bytes.
How many bits are in the address? 32
How many bits are in the offset field? 4
How many bits are in the tag (or block) field? 32 – 4 = 28
How many lines are in the cache? (210 bytes/cache) / (24 bytes/line) = 26 lines/cache
A request is made for the byte at address 0x12345678. What is the tag?

## Slide 28: Example Problem 6 Step 2 Answer
A system with 232 bytes of main memory has a fully associative cache with 210 bytes and a line size of 24 bytes.
How many bits are in the address? 32
How many bits are in the offset field? 4
How many bits are in the tag (or block) field? 32 – 4 = 28
How many lines are in the cache? (210 bytes/cache) / (24 bytes/line) = 26 lines/cache
A request is made for the byte at address 0x12345678. What is the tag?
0x1234567 (all but lowest 4 bits)

## Slide 29: Example Problem 7
A system with 216 bytes in the main memory. It has a fully associative cache with 25 bytes and a line size of 22 bytes.
The cache state is currently as below.
 | Line byte 1 | Line byte 2 | Line byte 2 | Line byte 4 | Line byte 3 |  | Line byte 4 | 
Tag | Offset | Data | Offset | Data | Offset | Data | Offset | data
11010101110010 | 00 | 10101010 | 01 | 00010010 | 10 | 00111110 | 11 | 00100001
10111111000000 | 00 | 10010011 | 01 | 11110000 | 10 | 01010100 | 11 | 10101011
00000000000001 | 00 | 11111111 | 01 | 00000000 | 10 | 11111100 | 11 | 00000011
01111110100110 | 00 | 10101010 | 01 | 01010101 | 10 | 00000000 | 11 | 00000000
There is a request for address 0x0007. Is it a hit or miss? 00000000000001 11
If it is a hit, what is returned? If it is a miss, what is the state of the cache after the data is obtained from main memory?

## Slide 30: Example Problem 7 Answer
A system with 216 bytes in the main memory. It has a fully associative cache with 25 bytes and a line size of 22 bytes.
The cache state is currently as below.
 | Line byte 1 | Line byte 2 | Line byte 2 | Line byte 4 | Line byte 3 |  | Line byte 4 | 
Tag | Offset | Data | Offset | Data | Offset | Data | Offset | data
11010101110010 | 00 | 10101010 | 01 | 00010010 | 10 | 00111110 | 11 | 00100001
10111111000000 | 00 | 10010011 | 01 | 11110000 | 10 | 01010100 | 11 | 10101011
00000000000001 | 00 | 11111111 | 01 | 00000000 | 10 | 11111100 | 11 | 00000011
01111110100110 | 00 | 10101010 | 01 | 01010101 | 10 | 00000000 | 11 | 00000000
There is a request for address 0x0007. Is it a hit or miss? Address is 16 bites, Offset = log(22) = 2 bits, tag = 14 bits
Address = 0000 0000 0000 0111 tag = 00000000000001 that is a hit, offset = 11, value returned = 00000011

## Slide 31: Example Problem 7 Step 2
A system with 216 bytes in the main memory. It has a fully associative cache with 25 bytes and a line size of 22 bytes.
The cache state is currently as below.
 | Line byte 1 | Line byte 2 | Line byte 2 | Line byte 4 | Line byte 3 |  | Line byte 4 | 
Tag | Offset | Data | Offset | Data | Offset | Data | Offset | data
11010101110010 | 00 | 10101010 | 01 | 00010010 | 10 | 00111110 | 11 | 00100001
10111111000000 | 00 | 10010011 | 01 | 11110000 | 10 | 01010100 | 11 | 10101011
00000000000001 | 00 | 11111111 | 01 | 00000000 | 10 | 11111100 | 11 | 00000011
01111110100110 | 00 | 10101010 | 01 | 01010101 | 10 | 00000000 | 11 | 00000000
There is a request for address 0xBB35. Is it a hit or miss? 10111011001101 01
If it is a hit, what is returned? If it is a miss, what is the state of the cache after the data is obtained from main memory?

## Slide 32: Example Problem 7 Step 2 Answer
A system with 216 bytes in the main memory. It has a fully associative cache with 25 bytes and a line size of 22 bytes.
The cache state is currently as below.
 | Line byte 1 | Line byte 2 | Line byte 2 | Line byte 4 | Line byte 3 |  | Line byte 4 | 
Tag | Offset | Data | Offset | Data | Offset | Data | Offset | data
11010101110010 | 00 | 10101010 | 01 | 00010010 | 10 | 00111110 | 11 | 00100001
10111111000000 | 00 | 10010011 | 01 | 11110000 | 10 | 01010100 | 11 | 10101011
00000000000001 | 00 | 11111111 | 01 | 00000000 | 10 | 11111100 | 11 | 00000011
01111110100110 | 00 | 10101010 | 01 | 01010101 | 10 | 00000000 | 11 | 00000000
There is a request for address 0xBB35. Is it a hit or miss?
1011 1011 0011 0101, tag = 10111011001101 a miss
This block is fetched from main memory and placed in the next line of the cache

## Slide 33: Example Problem 7 Step 3
A system with 216 bytes in the main memory. It has a fully associative cache with 25 bytes and a line size of 22 bytes.
The cache state is currently as below.
 | Line byte 1 | Line byte 2 | Line byte 2 | Line byte 4 | Line byte 3 |  | Line byte 4 | 
Tag | Offset | Data | Offset | Data | Offset | Data | Offset | data
11010101110010 | 00 | 10101010 | 01 | 00010010 | 10 | 00111110 | 11 | 00100001
10111111000000 | 00 | 10010011 | 01 | 11110000 | 10 | 01010100 | 11 | 10101011
00000000000001 | 00 | 11111111 | 01 | 00000000 | 10 | 11111100 | 11 | 00000011
01111110100110 | 00 | 10101010 | 01 | 01010101 | 10 | 00000000 | 11 | 00000000
10111011001101 | 00 | ???????? | 01 | ???????? | 10 | ????????? | 11 | ?????????
There is a request for address 0xBB35. Is it a hit or miss?
1011 1011 0011 0101, tag = 10111011001101 a miss
This block is fetched from main memory and placed in the next line of the cache