## Slide 1: Lookaside Cache

## Slide 2: Look Through Cache

## Slide 3: Example Problem
Consider a memory system with a 20ns access time supported by a cache with a 5ns access time and a hit rate of 90%
What is the average memory access time for a lookaside cache?
What is the average memory access time for a look through cache?

## Slide 4: Example Problem Answer
Consider a memory system with a 20ns access time supported by a cache with a 5ns access time and a hit rate of 90%
What is the average memory access time for a lookaside cache?
What is the average memory access time for a look through cache?
AMAT = 5*0.9 + 20*0.1 = 4.5+2 = 6.5ns
AMAT = 5 + 20*0.1 = 5+2 = 7ns

## Slide 5: Example Problem 2
Consider a memory system with a 20ns access time supported by a L1 cache with a 5ns access time and a hit rate of 90% and an L2 cache with an 8ns access time and a hit rate of 80%
What is the average memory access time for a lookaside cache?
What is the average memory access time for a look through cache?

## Slide 6: Example Problem 2 Answer
Consider a memory system with a 20ns access time supported by a L1 cache with a 5ns access time and a hit rate of 90% and an L2 cache with an 8ns access time and a hit rate of 80%
What is the average memory access time for a lookaside cache?
What is the average memory access time for a look through cache?
AMAT = 5*0.9 + 0.1*(8*0.8 + 20*0.2) = 4.5 + 0.1*(6.4+4) = 4.5 + 1.04 = 5.54 ns
AMAT = 5 + 0.1*(8 + 20*0.2) = 5 + 0.1*(8+4) = 5 + 1.2 = 6.2 ns

## Slide 7: Cache Organization

## Slide 8: Fully Associative

## Slide 9: Fully Associative

## Slide 10: Fully Associative

## Slide 11: Example Problem 3
A system has a main memory of 216 bytes and a fully associative cache that is 26 bytes. The block size is 23 bytes.
How many bits are in an address?
How many lines are in the cache?
What is the size of the offset field?
What is the size of the tag field?

## Slide 12: Example Problem 3 Answer
A system has a main memory of 216 bytes and a fully associative cache that is 26 bytes. The block size is 23 bytes.
How many bits are in an address? 16 bits
How many lines are in the cache? 26 bytes/cache / 23 bytes/line = 23 lines/cache
What is the width of the offset field? log(23) = 3 bits
What is the width of the tag field? 16-3 = 13 bits

## Slide 13: Example Problem 4
Say the state of the cache described in the last slide is as shown.
The following memory addresses are requested. For each, is it a hit? If it is a hit, what is the data requested?
0xED66
0x4A09
0x000F
Line | Tag | Data
0 | 0100101000001 | 0xABCDABCD0134D4E3
1 | 1011010011000 | 0x0122E4FAB237910A
2 | 1011001001001 | 0x01332E4F7A37910A
3 | 1100101010101 | 0x013325698AC7910C
4 | 1010101010101 | 0xABCD1298AC7910CA
5 | 1101101101000 | 0x214FAB237910A2C9
6 | 1011101101011 | 0x0122E4FAB2C3FA32
7 | 1110110101100 | 0xAB237910A2CC2454
8 | 1111111111111 | 0x1489BCD0134D4E3E
9 | 0000000000000 | 0x1AB34134D4E3E149
10 | 1010111011110 | 0x2BB34134D4E3FC32
11 | 1101110111001 | 0xABCD1298AC7910CA
12 | 1101101111011 | 0x214FAB237910A2C9
13 | 1011001100111 | 0xCD5671037910A2C9
14 | 1011101110101 | 0x0122E4FAB2C3FA32
15 | 1011101101010 | 0xAB237910A2CC2454

## Slide 14: Example Problem 4 Answer
Say the state of the cache described in the last slide is as shown.
The following memory addresses are requested. For each, is it a hit? If it is a hit, what is the data requested?
0xED66
1110 1101 0110 0110
1110110101100 110
tag = 1110110101100 = hit in line 7
line = 0xAB237910A2CC2454
offset = 6 = 0xAB237910A2CC2454
(assume little endian)
Line | Tag | Data
0 | 0100101000001 | 0xABCDABCD0134D4E3
1 | 1011010011000 | 0x0122E4FAB237910A
2 | 1011001001001 | 0x01332E4F7A37910A
3 | 1100101010101 | 0x013325698AC7910C
4 | 1010101010101 | 0xABCD1298AC7910CA
5 | 1101101101000 | 0x214FAB237910A2C9
6 | 1011101101011 | 0x0122E4FAB2C3FA32
7 | 1110110101100 | 0xAB237910A2CC2454
8 | 1111111111111 | 0x1489BCD0134D4E3E
9 | 0000000000000 | 0x1AB34134D4E3E149
10 | 1010111011110 | 0x2BB34134D4E3FC32
11 | 1101110111001 | 0xABCD1298AC7910CA
12 | 1101101111011 | 0x214FAB237910A2C9
13 | 1011001100111 | 0xCD5671037910A2C9
14 | 1011101110101 | 0x0122E4FAB2C3FA32
15 | 1011101101010 | 0xAB237910A2CC2454

## Slide 15: Example Problem 4 Answer Part 2
Say the state of the cache described in the last slide is as shown.
The following memory addresses are requested. For each, is it a hit? If it is a hit, what is the data requested?
0x4A09
0100 1010 0000 1001
0100101000001 001
tag = 0100101000001 = hit in line 0
line = 0xABCDABCD0134D4E3
offset = 1 = 0xABCDABCD0134D4E3
Line | Tag | Data
0 | 0100101000001 | 0xABCDABCD0134D4E3
1 | 1011010011000 | 0x0122E4FAB237910A
2 | 1011001001001 | 0x01332E4F7A37910A
3 | 1100101010101 | 0x013325698AC7910C
4 | 1010101010101 | 0xABCD1298AC7910CA
5 | 1101101101000 | 0x214FAB237910A2C9
6 | 1011101101011 | 0x0122E4FAB2C3FA32
7 | 1110110101100 | 0xAB237910A2CC2454
8 | 1111111111111 | 0x1489BCD0134D4E3E
9 | 0000000000000 | 0x1AB34134D4E3E149
10 | 1010111011110 | 0x2BB34134D4E3FC32
11 | 1101110111001 | 0xABCD1298AC7910CA
12 | 1101101111011 | 0x214FAB237910A2C9
13 | 1011001100111 | 0xCD5671037910A2C9
14 | 1011101110101 | 0x0122E4FAB2C3FA32
15 | 1011101101010 | 0xAB237910A2CC2454

## Slide 16: Example Problem 4 Answer Part 3
Say the state of the cache described in the last slide is as shown.
The following memory addresses are requested. For each, is it a hit? If it is a hit, what is the data requested?
0x000F
0000 0000 0000 1111
0000000000001 111
tag = 0000000000001 = miss
Line | Tag | Data
0 | 0100101000001 | 0xABCDABCD0134D4E3
1 | 1011010011000 | 0x0122E4FAB237910A
2 | 1011001001001 | 0x01332E4F7A37910A
3 | 1100101010101 | 0x013325698AC7910C
4 | 1010101010101 | 0xABCD1298AC7910CA
5 | 1101101101000 | 0x214FAB237910A2C9
6 | 1011101101011 | 0x0122E4FAB2C3FA32
7 | 1110110101100 | 0xAB237910A2CC2454
8 | 1111111111111 | 0x1489BCD0134D4E3E
9 | 0000000000000 | 0x1AB34134D4E3E149
10 | 1010111011110 | 0x2BB34134D4E3FC32
11 | 1101110111001 | 0xABCD1298AC7910CA
12 | 1101101111011 | 0x214FAB237910A2C9
13 | 1011001100111 | 0xCD5671037910A2C9
14 | 1011101110101 | 0x0122E4FAB2C3FA32
15 | 1011101101010 | 0xAB237910A2CC2454

## Slide 17: Direct Mapped

## Slide 18: Direct Mapped

## Slide 19: Example Problem 5
cache
line | tag | data
00 |  | 
01 |  | 
10 |  | 
11 |  | 
main memory
address
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
A system has 24 bytes of main memory and a direct mapped cache with 8 bytes.
A line is 2 bytes.
Address = 4 bits
Offset field = log(2) = 1 bit
Number of lines in cache =
(8 bytes/cache) / (2 bytes/line) = 4 lines/cache
Line field = log(4) = 2 bits
Tag field = 4 - 1 - 2 = 1 bit
For address 1010 what are the offset, line, and tag fields?
1010 = 1 01 0
tag = 1, line = 01, offset = 0

## Slide 20: Example Problem 5 Explanation
cache
line | tag | data
00 |  | 
01 |  | 
10 |  | 
11 |  | 
main memory
address
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
A system has 24 bytes of main memory and a direct mapped cache with 8 bytes.
A line is 2 bytes.
Address = 4 bits
Offset field = log(2) = 1 bit
Number of lines in cache =
(8 bytes/cache) / (2 bytes/line) = 4 lines/cache
Line field = log(4) = 2 bits
Tag field = 4 - 1 - 2 = 1 bit
For address 1010 what are the offset, line, and tag fields?
1010 = 1 01 0
tag = 1, line = 01, offset = 0

## Slide 21: Example Problem 6
line | tag | data
00 | 1 | 0xACD7
01 | 0 | 0x1243
10 | 0 | 0xA398
11 | 1 | 0x72AC
cache
Say the state of the cache described in the last slide is as shown.
The following memory addresses are requested. For each, is it a hit? If it is a hit, what is the data requested?
0xA
0xF
0x3

## Slide 22: Example Problem 6 Step 1
line | tag | data
00 | 1 | 0xACD7
01 | 0 | 0x1243
10 | 0 | 0xA398
11 | 1 | 0x72AC
cache
Say the state of the cache described in the last slide is as shown.
The following memory addresses are requested. For each, is it a hit? If it is a hit, what is the data requested?
0xA
1010
tag = 1, line = 01, offset = 0 miss

## Slide 23: Example Problem 6 Step 2
line | tag | data
00 | 1 | 0xACD7
01 | 0 | 0x1243
10 | 0 | 0xA398
11 | 1 | 0x72AC
cache
Say the state of the cache described in the last slide is as shown.
The following memory addresses are requested. For each, is it a hit? If it is a hit, what is the data requested?
0xF
1111
tag = 1 line = 11 offset = 1 --- hit
data = 0x72AC

## Slide 24: Example Problem 6 Step 3
line | tag | data
00 | 1 | 0xACD7
01 | 0 | 0x1243
10 | 0 | 0xA398
11 | 1 | 0x72AC
cache
Say the state of the cache described in the last slide is as shown.
The following memory addresses are requested. For each, is it a hit? If it is a hit, what is the data requested?
0x3
0011
tag = 0, line = 01, offset = 1 --- hit
data = 0x1243

## Slide 25: Example Problem 7
A system has a main memory with 232 bytes and a direct mapped cache with 212 bytes and a block size of 25 bytes.
What is the size of the address?
What is the size of the offset field?
What is the size of the line field?
What is the size of the tag field?

## Slide 26: Example Problem 7 Answer
A system has a main memory with 232 bytes and a direct mapped cache with 212 bytes and a block size of 25 bytes.
What is the size of the address? 32 bits
What is the size of the offset field? log(25) = 5 bits
What is the size of the line field? 212 bytes/cache / 25 bytes/line = 27 lines/cache
log(27) = 7 bits
What is the size of the tag field? 32-7-5 = 20 bits