## Slide 1: Digital Logic
A | B | C
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Express the truth table as the product of sums:
Use boolean algebra to derive the sum of products

## Slide 2: Digital Logic
A | B | C
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Express the truth table as the product of sums:
C = (A+B’) * (A’+B)
Use boolean algebra to derive the sum of products
C = (A’*A + A*B + A’*B’ + B’*B)
= (A’*B’ + A*B)

## Slide 3: Digital Logic
Write the truth table for this circuit
Write the equation for this circuit using product of sums or sum of products

## Slide 4: Digital Logic
Write the truth table for this circuit
(A+B)’
A | B | C | Z
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 

## Slide 5: Digital Logic
Write the truth table for this circuit
(A+B)’+(B*C)’
A | B | C | Z
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 

## Slide 6: Digital Logic
Write the truth table for this circuit
(A+B)’+(B*C)’+(A*C)
A | B | C | Z
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 

## Slide 7: Digital Logic
Write the truth table for this circuit
(A+B)’ + (B*C)’ + (A*C) = (A’*B’) + (B’ + C’) + A*C
A | B | C | Z
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 

## Slide 8: Digital Logic
Write the truth table for this circuit
(A+B)’ + (B*C)’ + (A*C) = (A’*B’) + (B’ + C’) + A*C
A | B | C | Z
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 

## Slide 9: Digital Logic
Write the truth table for this circuit
(A+B)’ + (B*C)’ + (A*C) = (A’*B’) + (B’ + C’) + A*C
A | B | C | Z
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 10: Digital Logic
Write the truth table for this circuit
(A+B)’ + (B*C)’ + (A*C) = (A’*B’) + (B’ + C’) + A*C
A | B | C | Z
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 11: Digital Logic
Write the truth table for this circuit
(A+B)’ + (B*C)’ + (A*C) = (A’*B’) + (B’ + C’) + A*C
Write the equation for this circuit using product of sums or sum of products
A | B | C | Z
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Product of sums - A+B’+C’
Sum of products - A’B’C’ + A’B’C + A’BC’ + AB’C’ + AB’C + ABC’ + ABC

## Slide 12: Multiplexor
Multiplexor circuit
  Selects one data channel (from many input channels)
0
1
2
3
2
OUTPUT LINES
INPUT DATA LINES
CONTROL LINES

## Slide 13: Multiplexor
Multiplexor circuit
  Selects one data channel (from many input channels)
  Maps the selected channel to the output channel
Sum-of-Products circuit
D1 … D4: Data channels
A, B: Control lines
F: Output channel
n control lines allows 2n inputs
Example: To select D1: A,B=0

## Slide 14: If you need a multiplexor to choose which of 5 inputs, how many control lines do you need?

## Slide 15: If you need a multiplexor to choose which of 5 inputs, how many control lines do you need? The ceiling of log(5) = 3, so you would need 3 control lines

## Slide 16: Decoder
Decoder circuit
  Given n control lines
  Select one of 2n outputs to activate
3
CONTROL LINES
OUTPUTS - ONE IS ACTIVATED

## Slide 17: Decoder
Decoder circuit
  Given n control lines
  Select one of 2n outputs to activate
Simple AND-gate circuit
D1 … D8 : Output channels
A, B, C : Control lines
Note: n control lines, 2n outputs
Laws of Boolean Logic
Regulate circuit function
Identity Law 1  A = A, A{0,1}
Example: Select D3: A, B, C = 0,1,1

## Slide 18: If your decoder selects from among 40 outputs how many control lines does it need?

## Slide 19: If your decoder selects from among 40 outputs how many control lines does it need? The ceiling of log(40) = 6, so 6 control lines are needed If you want to select the output channel 33, what should your control signals be?

## Slide 20: If your decoder selects from among 40 outputs how many control lines does it need? The ceiling of log(40) = 6, so 6 control lines are needed If you want to select the output channel 33, what should your control signals be? 100001 Selecting a byte from memory is basically using a decoder. 32 bit memory addresses are used to select from 232 addresses in memory

## Slide 21: Comparator
Comparator circuit
  Given two n-bit vectors A and B
  Output 1 if A = B, or 0 otherwise
A
B

## Slide 22: Comparator
Comparator circuit
  Given two n-bit vectors A and B
  Output 1 if A = B, or 0 otherwise
Simple XOR-gate circuit
A0, A1, …, AN-1 : Input vector #1
B0, B1, …, BN-1 : Input vector #2
Note: NOR gate combines N XOR gate outputs
Laws of Boolean Logic
Example: Comparator for Bit i outputs 0 if Ai = Bi
If all inputs to this NOR gate are zero, output is 1

## Slide 23: Majority vote circuit
Majority Function
  Returns 1 if a majority of inputs are high (=1)
  Formula: M(A,B,C) = A’BC + AB’C + ABC’ + ABC
  Truth Table  SOP Circuit:
  [Note: A = NOT(A)]
Application: In the Space Shuttle, 3 redundant circuits each compute the same function f. If a MAJORITY of circuit outputs agree (=1), then the 1-valued result is assumed to be correct.