## Slide 1: Examlet 2 Review
CDA3101
15 September 2022

## Slide 2: Examlet 2 Review
Sum of products / product of sums
Specialty circuits
  Multiplexor, Decoder, Majority, Comparator
Translate from ARM machine code to assembly and vice versa

## Slide 3: Digital Logic
A | B | C | Z
0 | 0 | 0 | 1
0 | 1 | 0 | 0
1 | 0 | 0 | 0
1 | 1 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 1
1 | 1 | 1 | 0
Express the truth table as the sum of products:

## Slide 4: Digital Logic
A | B | C | Z
0 | 0 | 0 | 1
0 | 1 | 0 | 0
1 | 0 | 0 | 0
1 | 1 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 1
1 | 1 | 1 | 0
Express the truth table as the sum of products:

## Slide 5: Digital Logic
A | B | C | Z
0 | 0 | 0 | 1
0 | 1 | 0 | 0
1 | 0 | 0 | 0
1 | 1 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 1
1 | 1 | 1 | 0
Express the truth table as the sum of products:
A’*B’*C’
A*B*C’
A’*B*C
A*B’*C

## Slide 6: Digital Logic
A | B | C | Z
0 | 0 | 0 | 1
0 | 1 | 0 | 0
1 | 0 | 0 | 0
1 | 1 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 1
1 | 1 | 1 | 0
Express the truth table as the sum of products:
Z = A’*B’*C’ + A*B*C’ + A’*B*C + A*B’*C
A’*B’*C’
A*B*C’
A’*B*C
A*B’*C

## Slide 7: Digital Logic
A | B | C | Z
0 | 0 | 0 | 1
0 | 1 | 0 | 0
1 | 0 | 0 | 0
1 | 1 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 1
1 | 1 | 1 | 0
Express the truth table as the product of sums:

## Slide 8: Digital Logic
A | B | C | Z
0 | 0 | 0 | 1
0 | 1 | 0 | 0
1 | 0 | 0 | 0
1 | 1 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 1
1 | 1 | 1 | 0
Express the truth table as the product of sums:

## Slide 9: Digital Logic
A | B | C | Z
0 | 0 | 0 | 1
0 | 1 | 0 | 0
1 | 0 | 0 | 0
1 | 1 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 1
1 | 1 | 1 | 0
Express the truth table as the product of sums:
A+B’+C
A’+B+C
A+B+C’
A’+B’+C’

## Slide 10: Digital Logic
A | B | C | Z
0 | 0 | 0 | 1
0 | 1 | 0 | 0
1 | 0 | 0 | 0
1 | 1 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 1
1 | 1 | 1 | 0
Express the truth table as the product of sums:
Z = (A+B’+C) * (A’+B+C) * (A+B+C’) * (A’+B’+C’)
A+B’+C
A’+B+C
A+B+C’
A’+B’+C’

## Slide 11: Multiplexor
Multiplexor circuit
  Selects one data channel (from many input channels)
0
1
2
3
2
OUTPUT LINES
INPUT DATA LINES
CONTROL LINES

## Slide 12: Multiplexor
Multiplexor circuit
  Selects one data channel (from many input channels)
  Maps the selected channel to the output channel
Sum-of-Products circuit
D1 … D4: Data channels
A, B: Control lines
F: Output channel
n control lines allows 2n inputs
Example: To select D1: A,B=0

## Slide 13: If you need a multiplexor to choose which of 5 inputs, how many control lines do you need?

## Slide 14: If you need a multiplexor to choose which of 5 inputs, how many control lines do you need? The ceiling of log(5) = 3, so you would need 3 control lines

## Slide 15: Decoder
Decoder circuit
  Given n control lines
  Select one of 2n outputs to activate
3
CONTROL LINES
OUTPUTS - ONE IS ACTIVATED

## Slide 16: Decoder
Decoder circuit
  Given n control lines
  Select one of 2n outputs to activate
Simple AND-gate circuit
D1 … D8 : Output channels
A, B, C : Control lines
Note: n control lines, 2n outputs
Laws of Boolean Logic
Regulate circuit function
Identity Law 1  A = A, A{0,1}
Example: Select D3: A, B, C = 0,1,1

## Slide 17: If your decoder selects from among 40 outputs how many control lines does it need?

## Slide 18: If your decoder selects from among 40 outputs how many control lines does it need? The ceiling of log(40) = 6, so 6 control lines are needed If you want to select the output channel 33, what should your control signals be?

## Slide 19: If your decoder selects from among 40 outputs how many control lines does it need? The ceiling of log(40) = 6, so 6 control lines are needed If you want to select the output channel 33, what should your control signals be? 100001 Selecting a byte from memory is basically using a decoder. 32 bit memory addresses are used to select from 232 addresses in memory

## Slide 20: Comparator
Comparator circuit
  Given two n-bit vectors A and B
  Output 1 if A = B, or 0 otherwise
A
B

## Slide 21: Comparator
Comparator circuit
  Given two n-bit vectors A and B
  Output 1 if A = B, or 0 otherwise
Simple XOR-gate circuit
A0, A1, …, AN-1 : Input vector #1
B0, B1, …, BN-1 : Input vector #2
Note: NOR gate combines N XOR gate outputs
Laws of Boolean Logic
Example: Comparator for Bit i outputs 0 if Ai = Bi
If all inputs to this NOR gate are zero, output is 1

## Slide 22: Majority vote circuit
Majority Function
  Returns 1 if a majority of inputs are high (=1)
  Formula: M(A,B,C) = A’BC + AB’C + ABC’ + ABC
  Truth Table  SOP Circuit:
  [Note: A = NOT(A)]
Application: In the Space Shuttle, 3 redundant circuits each compute the same function f. If a MAJORITY of circuit outputs agree (=1), then the 1-valued result is assumed to be correct.

## Slide 23: ARM ISA: R-format instruction
STRUCTURE OF AN R-format INSTRUCTION
Instruction Fields:
Field Explanation:
  opcode - basic operation of the instruction
  rm – second source register
  shamt – shift amount
  rn – first source register
  rd destination register
opcode rm shamt rn rd
11 bits 5 bits 6 bits 5 bits 5 bits

## Slide 24: Sample problem
What is the 32 bit machine code corresponding to
LSL X10, X9, #3
(Look at reference sheet)
Opcode = 11010011011, Format = R

## Slide 25: Sample problem
What is the 32 bit machine code corresponding to
LSL X10, X9, #3
(Look at reference sheet)
Opcode = 11010011011, Format = R, Rn is shifted and placed in Rd

## Slide 26: Sample problem
What is the 32 bit machine code corresponding to
LSL X10, X9, #3
(Look at reference sheet)
Opcode = 11010011011, Format = R, RN shifted and placed in RD
11010011011 00000 000011 01001 01010
Rm is not used
shamt = shift amount = 3
Rd
Rn

## Slide 27: Sample problem
What is the 32 bit machine code corresponding to
LSL X10, X9, #3
(Look at reference sheet)
Opcode = 11010011011, Format = R, RN shifted and placed in RD
11010011011 00000 000011 01001 01010
11010011011000000000110100101010
1101 0011 0110 0000 0000 1101 0010 1010
0xD3600D2A

## Slide 28: ARM ISA: R-format instruction
ADD X9, X10, X11  X9 = X10+X11
opcode rm shamt rn rd
11 bits 5 bits 6 bits 5 bits 5 bits
10001011000 01011 000000 01010 01001
SUB X9, X10, X11  X9 = X10-X11
opcode rm shamt rn rd
11 bits 5 bits 6 bits 5 bits 5 bits
11001011000 01011 000000 01010 01001

## Slide 29: ARM ISA: I-format instruction
Field Explanation:
  opcode - basic operation of the instruction
  Immediate – value of operand
  rn – source register
  rd destination register
opcode immediate rn rd
10 bits 12 bits 5 bits 5 bits

## Slide 30: ARM ISA: I-Type Instructions
ADDI X9, X10, #100  X9 = X10+100
opcode immediate rn rd
10 bits 12 bits 5 bits 5 bits
1001000100 000001100100 01010 01001

## Slide 31: Sample Problem
What is the ARM assembly language instruction corresponding to
0x8A150293

## Slide 32: Sample Problem
What is the ARM assembly language instruction corresponding to
0x8A150293
1000 1010 0001 0101 0000 0010 1001 0011

## Slide 33: Sample Problem
What is the ARM assembly language instruction corresponding to
0x8A150293
10001010 0001 0101 0000 0010 1001 0011
The only opcode that starts with 10001010 is for AND
Therefore, this is an AND instruction, an R type

## Slide 34: Sample Problem
What is the ARM assembly language instruction corresponding to
0x8A150293
10001010000 10101 000000 10100 10011
opcode rm shamt rn rd
rm = 10101 = X21
rn = 10100 = X20
rd = 10011 = X19
AND X19, X20, X21

## Slide 35: Sample Problem
What is the ARM assembly language instruction corresponding to
0xD100C949

## Slide 36: Sample Problem
What is the ARM assembly language instruction corresponding to
0xD100C949
1101 0001 0000 0000 1100 1001 0100 1001

## Slide 37: Sample Problem
What is the ARM assembly language instruction corresponding to
0xD100C949
11010001 0000 0000 1100 1001 0100 1001
The only opcode that starts with 11010001 is for SUBI
Therefore, this is a SUBI instruction, an I type

## Slide 38: Sample Problem
What is the ARM assembly language instruction corresponding to
0xD100C949
1101000100 000000110010 01010 01001
opcode ALU imm. rn rd
ALU immediate = 000000110010 = 50
rn = 01010 = X10
rd = 01001 = X9
SUBI X9, X10, #50