## Slide 1: Virtual Memory and Parallel Processing Sample Problems

## Slide 2: First lets talk about the project
Parameters
  Cache design / associativity
  Cache size
  Block/line size
  Replacement strategy – LRU vs. first in first out

## Slide 3: First lets talk about the project – what kind of results should you expect?
Parameters
  Cache design / associativity
    As associativity goes up (i.e. more lines in a set), hit rate should go…..

## Slide 4: First lets talk about the project – what kind of results should you expect?
Parameters
  Cache design / associativity
    As associativity goes up (i.e. more lines in a set), hit rate should go…..up
      Fully associative should have the best hit rate, direct mapped should have the worst

## Slide 5: First lets talk about the project – what kind of results should you expect?
Parameters
  Cache design / associativity
    As associativity goes up (i.e. more lines in a set), hit rate should go…..up
      Fully associative should have the best hit rate, direct mapped should have the worst
  Cache size
    As cache size goes up (i.e. more bytes in the cache), hit rate should go…..

## Slide 6: First lets talk about the project – what kind of results should you expect?
Parameters
  Cache design / associativity
    As associativity goes up (i.e. more lines in a set), hit rate should go…..up
      Fully associative should have the best hit rate, direct mapped should have the worst
  Cache size
    As cache size goes up (i.e. more bytes in the cache), hit rate should go…..up
      More room in the cache should translate to more data in the cache, which should translate to more hits

## Slide 7: First lets talk about the project – what kind of results should you expect?
Parameters
  Cache design / associativity
    As associativity goes up (i.e. more lines in a set), hit rate should go…..up
      Fully associative should have the best hit rate, direct mapped should have the worst
  Cache size
    As cache size goes up (i.e. more bytes in the cache), hit rate should go…..up
      More room in the cache should translate to more data in the cache, which should translate to more hits
  Line/block size
    As block size goes up (i.e. more blocks in the cache), hit rate should go…..

## Slide 8: First lets talk about the project – what kind of results should you expect?
Parameters
  Cache design / associativity
    As associativity goes up (i.e. more lines in a set), hit rate should go…..up
      Fully associative should have the best hit rate, direct mapped should have the worst
  Cache size
    As cache size goes up (i.e. more bytes in the cache), hit rate should go…..up
      More room in the cache should translate to more data in the cache, which should translate to more hits
  Line/block size
    As block size goes up (i.e. more blocks in the cache), hit rate should go…..up
      Bigger blocks should translate to more hits
      This one may not be as pronounced as the first two

## Slide 9: First lets talk about the project – what kind of results should you expect?
Parameters
  Cache design / associativity
    As associativity goes up (i.e. more lines in a set), hit rate should go…..up
      Fully associative should have the best hit rate, direct mapped should have the worst
  Cache size
    As cache size goes up (i.e. more bytes in the cache), hit rate should go…..up
      More room in the cache should translate to more data in the cache, which should translate to more hits
  Line/block size
    As block size goes up (i.e. more blocks in the cache), hit rate should go…..up
      Bigger blocks should translate to more hits
      This one may not be as pronounced as the first two
  Replacement strategy
    LRU or FIFO, which one has a higher hit rate?
      Depends on the nature of the accesses, but LRU should be better
      The first few assignments turned in showed this to be the case

## Slide 10: First lets talk about the project – what kind of results should you expect?
Parameters
  Cache design / associativity
    As associativity goes up (i.e. more lines in a set), hit rate should go…..up
      Fully associative should have the best hit rate, direct mapped should have the worst
  Cache size
    As cache size goes up (i.e. more bytes in the cache), hit rate should go…..up
      More room in the cache should translate to more data in the cache, which should translate to more hits
  Line/block size
    As block size goes up (i.e. more blocks in the cache), hit rate should go…..up
      Bigger blocks should translate to more hits
      This one may not be as pronounced as the first two
  Replacement strategy
    LRU or FIFO, which one has a higher hit rate?
      Depends on the nature of the accesses, but LRU should be better
      The first few assignments turned in showed this to be the case
    Why use trace files? Why not just generate addresses randomly?

## Slide 11: 11
The following virtual bytes are requested:
0x223d, 0x58b3, 0x4ee6, 0x0049
For each access, is it a hit in the TLB?
Is it a hit in the page table?
A page fault?
What is the updated TLB?
What is the updated page table?
Translate to a physical address
Assume page sizes are 212 bytes
Virtual address space is 216 bytes, physical address space is 215 bytes
Valid | Tag / Frame | Physical Page Number | Last Access Time
1 | 0xb | 7 | 3
1 | 0x7 | 4 | 2
1 | 0xa | 3 | 9
1 | 0x4 | 1 | 7
Frame | Valid | Physical Page or in Disk | Last Access time
0 | 1 | 5 | 4
1 | 0 | disk | 
2 | 0 | disk | 
3 | 1 | 6 | 1
4 | 1 | 1 | 7
5 | 1 | 2 | 5
6 | 0 | disk | 
7 | 1 | 4 | 2
8 | 0 | disk | 
9 | 0 | disk | 
a | 1 | 3 | 9
b | 1 | 7 | 3
c | 0 | disk | 
d | 0 | disk | 
e | 1 | 0 | 10

## Slide 12: 12
The following virtual bytes are requested:
0x223d, 0x58b3, 0x4ee6, 0x0049
For each access, is it a hit in the TLB?
Is it a hit in the page table?
A page fault?
What is the updated page table?
What is the updated TLB?
Translate to a physical address
Assume page sizes are 212 bytes
Virtual address space is 216 bytes, physical address space is 215 bytes
Virtual addresses are log(216) = 16 bits
Physical addresses are log(215) = 15 bits
Offset field = log(212) = 12 bits
Frame / Tag = 16-12 = 4 bits (virtual address)
Page = 15-12 = 3 bits (physical address)
Valid | Tag / Frame | Physical Page Number | Last Access time
1 | 0xb | 7 | 3
1 | 0x7 | 4 | 2
1 | 0xa | 3 | 9
1 | 0x4 | 1 | 7
Frame | Valid | Physical Page or in Disk | Last Access time
0 | 1 | 5 | 4
1 | 0 | disk | 
2 | 0 | disk | 
3 | 1 | 6 | 1
4 | 1 | 1 | 7
5 | 1 | 2 | 5
6 | 0 | disk | 
7 | 1 | 4 | 2
8 | 0 | disk | 
9 | 0 | disk | 
a | 1 | 3 | 9
b | 1 | 7 | 3
c | 0 | disk | 
d | 0 | disk | 
e | 1 | 0 | 10

## Slide 13: 13
0x223d
Frame/tag = 0x2 (leftmost 4 bits)
For each access, is it a hit in the TLB? no
Is it a hit in the page table? no
A page fault? Yes
What is the updated page table?
What is the updated TLB?
Translate to a physical address
Assume page sizes are 212 bytes
Virtual address space is 216 bytes, physical address space is 215 bytes
Virtual addresses are log(216) = 16 bits
Physical addresses are log(215) = 15 bits
Offset field = log(212) = 12 bits
Frame / Tag = 16-12 = 4 bits (virtual address)
Page = 15-12 = 3 bits (physical address)
Valid | Tag / Frame | Physical Page Number | Last Access time
1 | 0xb | 7 | 3
1 | 0x7 | 4 | 2
1 | 0xa | 2 | 9
1 | 0x4 | 1 | 7
Frame | Valid | Physical Page or in Disk | Last Access time
0 | 1 | 5 | 4
1 | 0 | disk | 
2 | 0 | disk | 
3 | 1 | 6 | 1
4 | 1 | 1 | 7
5 | 1 | 2 | 5
6 | 0 | disk | 
7 | 1 | 4 | 2
8 | 0 | disk | 
9 | 0 | disk | 
a | 1 | 3 | 9
b | 1 | 7 | 3
c | 0 | disk | 
d | 0 | disk | 
e | 1 | 0 | 10

## Slide 14: 14
0x223d
Frame/tag = 0x2 (leftmost 4 bits)
For each access, is it a hit in the TLB? no
Is it a hit in the page table? no
A page fault? Yes
What is the updated page table?
What is the updated TLB?
Translate to a physical address
Assume page sizes are 212 bytes
Virtual address space is 216 bytes, physical address space is 215 bytes
Virtual addresses are log(216) = 16 bits
Physical addresses are log(215) = 15 bits
Offset field = log(212) = 12 bits
Frame / Tag = 16-12 = 4 bits (virtual address)
Page = 15-12 = 3 bits (physical address)
Valid | Tag / Frame | Physical Page Number | Last Access time
1 | 0xb | 7 | 3
1 | 0x7 | 4 | 2
1 | 0xa | 3 | 9
1 | 0x4 | 1 | 7
Frame | Valid | Physical Page or in Disk | Last Access time
0 | 1 | 5 | 4
1 | 0 | disk | 
2 | 1 | 6 | 11
3 | 0 | disk | 
4 | 1 | 1 | 7
5 | 1 | 2 | 5
6 | 0 | disk | 
7 | 1 | 4 | 2
8 | 0 | disk | 
9 | 0 | disk | 
a | 1 | 3 | 9
b | 1 | 7 | 3
c | 0 | disk | 
d | 0 | disk | 
e | 1 | 0 | 10

## Slide 15: 15
0x223d
Frame/tag = 0x2 (leftmost 4 bits)
For each access, is it a hit in the TLB? no
Is it a hit in the page table? no
A page fault? Yes
What is the updated page table?
What is the updated TLB?
Translate to a physical address
Assume page sizes are 212 bytes
Virtual address space is 216 bytes, physical address space is 215 bytes
Virtual addresses are log(216) = 16 bits
Physical addresses are log(215) = 15 bits
Offset field = log(212) = 12 bits
Frame / Tag = 16-12 = 4 bits (virtual address)
Page = 15-12 = 3 bits (physical address)
Valid | Tag / Frame | Physical Page Number | Last Access time
1 | 0xb | 7 | 3
1 | 0x7 | 4 | 2
1 | 0xa | 3 | 9
1 | 0x4 | 1 | 7
Frame | Valid | Physical Page or in Disk | Last Access time
0 | 1 | 5 | 4
1 | 0 | disk | 
2 | 1 | 6 | 11
3 | 0 | disk | 
4 | 1 | 1 | 7
5 | 1 | 2 | 5
6 | 0 | disk | 
7 | 1 | 4 | 2
8 | 0 | disk | 
9 | 0 | disk | 
a | 1 | 3 | 9
b | 1 | 7 | 3
c | 0 | disk | 
d | 0 | disk | 
e | 1 | 0 | 10

## Slide 16: 16
0x223d
Frame/tag = 0x2 (leftmost 4 bits)
For each access, is it a hit in the TLB? no
Is it a hit in the page table? no
A page fault? Yes
What is the updated page table?
What is the updated TLB?
Translate to a physical address
Assume page sizes are 212 bytes
Virtual address space is 216 bytes, physical address space is 215 bytes
Virtual addresses are log(216) = 16 bits
Physical addresses are log(215) = 15 bits
Offset field = log(212) = 12 bits
Frame / Tag = 16-12 = 4 bits (virtual address)
Page = 15-12 = 3 bits (physical address)
Valid | Tag / Frame | Physical Page Number | Last Access time
1 | 0xb | 7 | 3
1 | 0x2 | 6 | 11
1 | 0xa | 3 | 9
1 | 0x4 | 1 | 7
Frame | Valid | Physical Page or in Disk | Last Access time
0 | 1 | 5 | 4
1 | 0 | disk | 
2 | 1 | 6 | 11
3 | 0 | disk | 
4 | 1 | 1 | 7
5 | 1 | 2 | 5
6 | 0 | disk | 
7 | 1 | 4 | 2
8 | 0 | disk | 
9 | 0 | disk | 
a | 1 | 3 | 9
b | 1 | 7 | 3
c | 0 | disk | 
d | 0 | disk | 
e | 1 | 0 | 10

## Slide 17: 17
0x223d
Frame/tag = 0x2 (leftmost 4 bits)
For each access, is it a hit in the TLB? no
Is it a hit in the page table? no
A page fault? Yes
What is the updated page table?
What is the updated TLB?
Translate to a physical address
0x623d -> 110 0010 0011 1011
Assume page sizes are 212 bytes
Virtual address space is 216 bytes, physical address space is 215 bytes
Virtual addresses are log(216) = 16 bits
Physical addresses are log(215) = 15 bits
Offset field = log(212) = 12 bits
Frame / Tag = 16-12 = 4 bits (virtual address)
Page = 15-12 = 3 bits (physical address)
Valid | Tag / Frame | Physical Page Number | Last Access time
1 | 0xb | 7 | 3
1 | 0x2 | 6 | 11
1 | 0xa | 3 | 9
1 | 0x4 | 1 | 7
Frame | Valid | Physical Page or in Disk | Last Access time
0 | 1 | 5 | 4
1 | 0 | disk | 
2 | 1 | 6 | 11
3 | 0 | disk | 
4 | 1 | 1 | 7
5 | 1 | 2 | 5
6 | 0 | disk | 
7 | 1 | 4 | 2
8 | 0 | disk | 
9 | 0 | disk | 
a | 1 | 3 | 9
b | 1 | 7 | 3
c | 0 | disk | 
d | 0 | disk | 
e | 1 | 0 | 10

## Slide 18: 18
0x58b3
Frame/tag = 0x5 (leftmost 4 bits)
For each access, is it a hit in the TLB?
Is it a hit in the page table?
A page fault?
What is the updated page table?
What is the updated TLB?
Translate to a physical address
Assume page sizes are 212 bytes
Virtual address space is 216 bytes, physical address space is 215 bytes
Virtual addresses are log(216) = 16 bits
Physical addresses are log(215) = 15 bits
Offset field = log(212) = 12 bits
Frame / Tag = 16-12 = 4 bits (virtual address)
Page = 15-12 = 3 bits (physical address)
Valid | Tag / Frame | Physical Page Number | Last Access time
1 | 0xb | 7 | 3
1 | 0x2 | 6 | 11
1 | 0xa | 3 | 9
1 | 0x4 | 1 | 7
Frame | Valid | Physical Page or in Disk | Last Access time
0 | 1 | 5 | 4
1 | 0 | disk | 
2 | 1 | 6 | 11
3 | 0 | disk | 
4 | 1 | 1 | 7
5 | 1 | 2 | 5
6 | 0 | disk | 
7 | 1 | 4 | 2
8 | 0 | disk | 
9 | 0 | disk | 
a | 1 | 3 | 9
b | 1 | 7 | 3
c | 0 | disk | 
d | 0 | disk | 
e | 1 | 0 | 10

## Slide 19: 19
0x58b3
Frame/tag = 0x5 (leftmost 4 bits)
For each access, is it a hit in the TLB? no
Is it a hit in the page table? yes
A page fault? no
What is the updated page table?
What is the updated TLB?
Translate to a physical address
Assume page sizes are 212 bytes
Virtual address space is 216 bytes, physical address space is 215 bytes
Virtual addresses are log(216) = 16 bits
Physical addresses are log(215) = 15 bits
Offset field = log(212) = 12 bits
Frame / Tag = 16-12 = 4 bits (virtual address)
Page = 15-12 = 3 bits (physical address)
Valid | Tag / Frame | Physical Page Number | Last Access time
1 | 0xb | 7 | 3
1 | 0x2 | 6 | 11
1 | 0xa | 3 | 9
1 | 0x4 | 1 | 7
Frame | Valid | Physical Page or in Disk | Last Access time
0 | 1 | 5 | 4
1 | 0 | disk | 
2 | 1 | 6 | 11
3 | 0 | disk | 
4 | 1 | 1 | 7
5 | 1 | 2 | 5
6 | 0 | disk | 
7 | 1 | 4 | 2
8 | 0 | disk | 
9 | 0 | disk | 
a | 1 | 3 | 9
b | 1 | 7 | 3
c | 0 | disk | 
d | 0 | disk | 
e | 1 | 0 | 10

## Slide 20: 20
0x58b3
Frame/tag = 0x5 (leftmost 4 bits)
For each access, is it a hit in the TLB? no
Is it a hit in the page table? yes
A page fault? no
What is the updated page table?
What is the updated TLB?
Translate to a physical address
Assume page sizes are 212 bytes
Virtual address space is 216 bytes, physical address space is 215 bytes
Virtual addresses are log(216) = 16 bits
Physical addresses are log(215) = 15 bits
Offset field = log(212) = 12 bits
Frame / Tag = 16-12 = 4 bits (virtual address)
Page = 15-12 = 3 bits (physical address)
Valid | Tag / Frame | Physical Page Number | Last Access time
1 | 0xb | 7 | 3
1 | 0x2 | 6 | 11
1 | 0xa | 3 | 9
1 | 0x4 | 1 | 7
Frame | Valid | Physical Page or in Disk | Last Access time
0 | 1 | 5 | 4
1 | 0 | disk | 
2 | 1 | 6 | 11
3 | 0 | disk | 
4 | 1 | 1 | 7
5 | 1 | 2 | 12
6 | 0 | disk | 
7 | 1 | 4 | 2
8 | 0 | disk | 
9 | 0 | disk | 
a | 1 | 3 | 9
b | 1 | 7 | 3
c | 0 | disk | 
d | 0 | disk | 
e | 1 | 0 | 10

## Slide 21: 21
0x58b3
Frame/tag = 0x5 (leftmost 4 bits)
For each access, is it a hit in the TLB? no
Is it a hit in the page table? yes
A page fault? no
What is the updated page table?
What is the updated TLB?
Translate to a physical address
Assume page sizes are 212 bytes
Virtual address space is 216 bytes, physical address space is 215 bytes
Virtual addresses are log(216) = 16 bits
Physical addresses are log(215) = 15 bits
Offset field = log(212) = 12 bits
Frame / Tag = 16-12 = 4 bits (virtual address)
Page = 15-12 = 3 bits (physical address)
Valid | Tag / Frame | Physical Page Number | Last Access time
1 | 0xb | 7 | 3
1 | 0x2 | 6 | 11
1 | 0xa | 3 | 9
1 | 0x4 | 1 | 7
Frame | Valid | Physical Page or in Disk | Last Access time
0 | 1 | 5 | 4
1 | 0 | disk | 
2 | 1 | 6 | 11
3 | 0 | disk | 
4 | 1 | 1 | 7
5 | 1 | 2 | 12
6 | 0 | disk | 
7 | 1 | 4 | 2
8 | 0 | disk | 
9 | 0 | disk | 
a | 1 | 3 | 9
b | 1 | 7 | 3
c | 0 | disk | 
d | 0 | disk | 
e | 1 | 0 | 10

## Slide 22: 22
0x58b3
Frame/tag = 0x5 (leftmost 4 bits)
For each access, is it a hit in the TLB? no
Is it a hit in the page table? yes
A page fault? no
What is the updated page table?
What is the updated TLB?
Translate to a physical address
Assume page sizes are 212 bytes
Virtual address space is 216 bytes, physical address space is 215 bytes
Virtual addresses are log(216) = 16 bits
Physical addresses are log(215) = 15 bits
Offset field = log(212) = 12 bits
Frame / Tag = 16-12 = 4 bits (virtual address)
Page = 15-12 = 3 bits (physical address)
Valid | Tag / Frame | Physical Page Number | Last Access time
1 | 0x5 | 2 | 12
1 | 0x2 | 6 | 11
1 | 0xa | 3 | 9
1 | 0x4 | 1 | 7
Frame | Valid | Physical Page or in Disk | Last Access time
0 | 1 | 5 | 4
1 | 0 | disk | 
2 | 1 | 6 | 11
3 | 0 | disk | 
4 | 1 | 1 | 7
5 | 1 | 2 | 12
6 | 0 | disk | 
7 | 1 | 4 | 2
8 | 0 | disk | 
9 | 0 | disk | 
a | 1 | 3 | 9
b | 1 | 7 | 3
c | 0 | disk | 
d | 0 | disk | 
e | 1 | 0 | 10

## Slide 23: 23
0x58b3
Frame/tag = 0x5 (leftmost 4 bits)
For each access, is it a hit in the TLB? no
Is it a hit in the page table? yes
A page fault? no
What is the updated page table?
What is the updated TLB?
Translate to a physical address
0x28b3 -> 010 1000 1011 0011
Assume page sizes are 212 bytes
Virtual address space is 216 bytes, physical address space is 215 bytes
Virtual addresses are log(216) = 16 bits
Physical addresses are log(215) = 15 bits
Offset field = log(212) = 12 bits
Frame / Tag = 16-12 = 4 bits (virtual address)
Page = 15-12 = 3 bits (physical address)
Valid | Tag / Frame | Physical Page Number | Last Access time
1 | 0x5 | 2 | 12
1 | 0x2 | 6 | 11
1 | 0xa | 3 | 9
1 | 0x4 | 1 | 7
Frame | Valid | Physical Page or in Disk | Last Access time
0 | 1 | 5 | 4
1 | 0 | disk | 
2 | 1 | 6 | 11
3 | 0 | disk | 
4 | 1 | 1 | 7
5 | 1 | 2 | 12
6 | 0 | disk | 
7 | 1 | 4 | 2
8 | 0 | disk | 
9 | 0 | disk | 
a | 1 | 3 | 9
b | 1 | 7 | 3
c | 0 | disk | 
d | 0 | disk | 
e | 1 | 0 | 10

## Slide 24: 24
0x4ee6
Frame/tag = 0x4
For each access, is it a hit in the TLB?
Is it a hit in the page table?
A page fault?
What is the updated page table?
What is the updated TLB?
Translate to a physical address
Assume page sizes are 212 bytes
Virtual address space is 216 bytes, physical address space is 215 bytes
Virtual addresses are log(216) = 16 bits
Physical addresses are log(215) = 15 bits
Offset field = log(212) = 12 bits
Frame / Tag = 16-12 = 4 bits (virtual address)
Page = 15-12 = 3 bits (physical address)
Valid | Tag / Frame | Physical Page Number | Last Access time
1 | 0x5 | 2 | 12
1 | 0x2 | 6 | 11
1 | 0xa | 3 | 9
1 | 0x4 | 1 | 7
Frame | Valid | Physical Page or in Disk | Last Access time
0 | 1 | 5 | 4
1 | 0 | disk | 
2 | 1 | 6 | 11
3 | 0 | disk | 
4 | 1 | 1 | 7
5 | 1 | 2 | 12
6 | 0 | disk | 
7 | 1 | 4 | 2
8 | 0 | disk | 
9 | 0 | disk | 
a | 1 | 3 | 9
b | 1 | 7 | 3
c | 0 | disk | 
d | 0 | disk | 
e | 1 | 0 | 10

## Slide 25: 25
0x4ee6
Frame/tag = 0x4
For each access, is it a hit in the TLB? yes
Is it a hit in the page table?
A page fault?
What is the updated page table?
What is the updated TLB?
Translate to a physical address
Assume page sizes are 212 bytes
Virtual address space is 216 bytes, physical address space is 215 bytes
Virtual addresses are log(216) = 16 bits
Physical addresses are log(215) = 15 bits
Offset field = log(212) = 12 bits
Frame / Tag = 16-12 = 4 bits (virtual address)
Page = 15-12 = 3 bits (physical address)
Valid | Tag / Frame | Physical Page Number | Last Access time
1 | 0x5 | 2 | 12
1 | 0x2 | 6 | 11
1 | 0xa | 3 | 9
1 | 0x4 | 1 | 7
Frame | Valid | Physical Page or in Disk | Last Access time
0 | 1 | 5 | 4
1 | 0 | disk | 
2 | 1 | 6 | 11
3 | 0 | disk | 
4 | 1 | 1 | 7
5 | 1 | 2 | 12
6 | 0 | disk | 
7 | 1 | 4 | 2
8 | 0 | disk | 
9 | 0 | disk | 
a | 1 | 3 | 9
b | 1 | 7 | 3
c | 0 | disk | 
d | 0 | disk | 
e | 1 | 0 | 10

## Slide 26: 26
0x4ee6
Frame/tag = 0x4
For each access, is it a hit in the TLB? yes
Is it a hit in the page table? yes
A page fault? no
What is the updated page table?
What is the updated TLB?
Translate to a physical address
Assume page sizes are 212 bytes
Virtual address space is 216 bytes, physical address space is 215 bytes
Virtual addresses are log(216) = 16 bits
Physical addresses are log(215) = 15 bits
Offset field = log(212) = 12 bits
Frame / Tag = 16-12 = 4 bits (virtual address)
Page = 15-12 = 3 bits (physical address)
Valid | Tag / Frame | Physical Page Number | Last Access time
1 | 0x5 | 2 | 12
1 | 0x2 | 6 | 11
1 | 0xa | 3 | 9
1 | 0x4 | 1 | 7
Frame | Valid | Physical Page or in Disk | Last Access time
0 | 1 | 5 | 4
1 | 0 | disk | 
2 | 1 | 6 | 11
3 | 0 | disk | 
4 | 1 | 1 | 7
5 | 1 | 2 | 12
6 | 0 | disk | 
7 | 1 | 4 | 2
8 | 0 | disk | 
9 | 0 | disk | 
a | 1 | 3 | 9
b | 1 | 7 | 3
c | 0 | disk | 
d | 0 | disk | 
e | 1 | 0 | 10

## Slide 27: 27
0x4ee6
Frame/tag = 0x4
For each access, is it a hit in the TLB? yes
Is it a hit in the page table? yes
A page fault? no
What is the updated page table?
What is the updated TLB?
Translate to a physical address
Assume page sizes are 212 bytes
Virtual address space is 216 bytes, physical address space is 215 bytes
Virtual addresses are log(216) = 16 bits
Physical addresses are log(215) = 15 bits
Offset field = log(212) = 12 bits
Frame / Tag = 16-12 = 4 bits (virtual address)
Page = 15-12 = 3 bits (physical address)
Valid | Tag / Frame | Physical Page Number | Last Access time
1 | 0x5 | 2 | 12
1 | 0x2 | 6 | 11
1 | 0xa | 3 | 9
1 | 0x4 | 1 | 13
Frame | Valid | Physical Page or in Disk | Last Access time
0 | 1 | 5 | 4
1 | 0 | disk | 
2 | 1 | 6 | 11
3 | 0 | disk | 
4 | 1 | 1 | 13
5 | 1 | 2 | 12
6 | 0 | disk | 
7 | 1 | 4 | 2
8 | 0 | disk | 
9 | 0 | disk | 
a | 1 | 3 | 9
b | 1 | 7 | 3
c | 0 | disk | 
d | 0 | disk | 
e | 1 | 0 | 10

## Slide 28: 28
0x4ee6
Frame/tag = 0x4
For each access, is it a hit in the TLB? yes
Is it a hit in the page table? yes
A page fault? no
What is the updated page table?
What is the updated TLB?
Translate to a physical address
0x1ee6 -> 001 1110 1110 0110
Assume page sizes are 212 bytes
Virtual address space is 216 bytes, physical address space is 215 bytes
Virtual addresses are log(216) = 16 bits
Physical addresses are log(215) = 15 bits
Offset field = log(212) = 12 bits
Frame / Tag = 16-12 = 4 bits (virtual address)
Page = 15-12 = 3 bits (physical address)
Valid | Tag / Frame | Physical Page Number | Last Access time
1 | 0x5 | 2 | 12
1 | 0x2 | 6 | 11
1 | 0xa | 3 | 9
1 | 0x4 | 1 | 13
Frame | Valid | Physical Page or in Disk | Last Access time
0 | 1 | 5 | 4
1 | 0 | disk | 
2 | 1 | 6 | 11
3 | 0 | disk | 
4 | 1 | 1 | 13
5 | 1 | 2 | 12
6 | 0 | disk | 
7 | 1 | 4 | 2
8 | 0 | disk | 
9 | 0 | disk | 
a | 1 | 3 | 9
b | 1 | 7 | 3
c | 0 | disk | 
d | 0 | disk | 
e | 1 | 0 | 10

## Slide 29: 29
0x0049
For each access, is it a hit in the TLB?
Is it a hit in the page table?
A page fault?
What is the updated page table?
What is the updated TLB?
Assume page sizes are 212 bytes
Virtual address space is 216 bytes, physical address space is 215 bytes
Virtual addresses are log(216) = 16 bits
Physical addresses are log(215) = 15 bits
Offset field = log(212) = 12 bits
Frame / Tag = 16-12 = 4 bits (virtual address)
Page = 15-12 = 3 bits (physical address)
Valid | Tag / Frame | Physical Page Number | Last Access time
1 | 0x5 | 2 | 12
1 | 0x2 | 6 | 11
1 | 0xa | 3 | 9
1 | 0x4 | 1 | 13
Frame | Valid | Physical Page or in Disk | Last Access time
0 | 1 | 5 | 4
1 | 0 | disk | 
2 | 1 | 6 | 11
3 | 0 | disk | 
4 | 1 | 1 | 13
5 | 1 | 2 | 12
6 | 0 | disk | 
7 | 1 | 4 | 2
8 | 0 | disk | 
9 | 0 | disk | 
a | 1 | 3 | 9
b | 1 | 7 | 3
c | 0 | disk | 
d | 0 | disk | 
e | 1 | 0 | 10

## Slide 30: 30
0x0049
Frame/tag = 0x0
For each access, is it a hit in the TLB? no
Is it a hit in the page table?
A page fault?
What is the updated page table?
What is the updated TLB?
Assume page sizes are 212 bytes
Virtual address space is 216 bytes, physical address space is 215 bytes
Virtual addresses are log(216) = 16 bits
Physical addresses are log(215) = 15 bits
Offset field = log(212) = 12 bits
Frame / Tag = 16-12 = 4 bits (virtual address)
Page = 15-12 = 3 bits (physical address)
Valid | Tag / Frame | Physical Page Number | Last Access time
1 | 0x5 | 2 | 12
1 | 0x2 | 6 | 11
1 | 0xa | 3 | 9
1 | 0x4 | 1 | 13
Frame | Valid | Physical Page or in Disk | Last Access time
0 | 1 | 5 | 4
1 | 0 | disk | 
2 | 1 | 6 | 11
3 | 0 | disk | 
4 | 1 | 1 | 13
5 | 1 | 2 | 12
6 | 0 | disk | 
7 | 1 | 4 | 2
8 | 0 | disk | 
9 | 0 | disk | 
a | 1 | 3 | 9
b | 1 | 7 | 3
c | 0 | disk | 
d | 0 | disk | 
e | 1 | 0 | 10

## Slide 31: 31
0x0049
Frame/tag = 0x0
For each access, is it a hit in the TLB? no
Is it a hit in the page table? yes
A page fault? no
What is the updated page table?
What is the updated TLB?
Assume page sizes are 212 bytes
Virtual address space is 216 bytes, physical address space is 215 bytes
Virtual addresses are log(216) = 16 bits
Physical addresses are log(215) = 15 bits
Offset field = log(212) = 12 bits
Frame / Tag = 16-12 = 4 bits (virtual address)
Page = 15-12 = 3 bits (physical address)
Valid | Tag / Frame | Physical Page Number | Last Access time
1 | 0x5 | 2 | 12
1 | 0x2 | 6 | 11
1 | 0xa | 3 | 9
1 | 0x4 | 1 | 13
Frame | Valid | Physical Page or in Disk | Last Access time
0 | 1 | 5 | 4
1 | 0 | disk | 
2 | 1 | 6 | 11
3 | 0 | disk | 
4 | 1 | 1 | 13
5 | 1 | 2 | 12
6 | 0 | disk | 
7 | 1 | 4 | 2
8 | 0 | disk | 
9 | 0 | disk | 
a | 1 | 3 | 9
b | 1 | 7 | 3
c | 0 | disk | 
d | 0 | disk | 
e | 1 | 0 | 10

## Slide 32: 32
0x0049
Frame/tag = 0x0
For each access, is it a hit in the TLB? no
Is it a hit in the page table? yes
A page fault? no
What is the updated page table?
What is the updated TLB?
Assume page sizes are 212 bytes
Virtual address space is 216 bytes, physical address space is 215 bytes
Virtual addresses are log(216) = 16 bits
Physical addresses are log(215) = 15 bits
Offset field = log(212) = 12 bits
Frame / Tag = 16-12 = 4 bits (virtual address)
Page = 15-12 = 3 bits (physical address)
Valid | Tag / Frame | Physical Page Number | Last Access time
1 | 0x5 | 2 | 12
1 | 0x2 | 6 | 11
1 | 0xa | 3 | 9
1 | 0x4 | 1 | 13
Frame | Valid | Physical Page or in Disk | Last Access time
0 | 1 | 5 | 14
1 | 0 | disk | 
2 | 1 | 6 | 11
3 | 0 | disk | 
4 | 1 | 1 | 13
5 | 1 | 2 | 12
6 | 0 | disk | 
7 | 1 | 4 | 2
8 | 0 | disk | 
9 | 0 | disk | 
a | 1 | 3 | 9
b | 1 | 7 | 3
c | 0 | disk | 
d | 0 | disk | 
e | 1 | 0 | 10

## Slide 33: 33
0x0049
Frame/tag = 0x0
For each access, is it a hit in the TLB? no
Is it a hit in the page table? yes
A page fault? no
What is the updated page table?
What is the updated TLB?
Assume page sizes are 212 bytes
Virtual address space is 216 bytes, physical address space is 215 bytes
Virtual addresses are log(216) = 16 bits
Physical addresses are log(215) = 15 bits
Offset field = log(212) = 12 bits
Frame / Tag = 16-12 = 4 bits (virtual address)
Page = 15-12 = 3 bits (physical address)
Valid | Tag / Frame | Physical Page Number | Last Access time
1 | 0x5 | 2 | 12
1 | 0x2 | 6 | 11
1 | 0xa | 3 | 9
1 | 0x4 | 1 | 13
Frame | Valid | Physical Page or in Disk | Last Access time
0 | 1 | 5 | 14
1 | 0 | disk | 
2 | 1 | 6 | 11
3 | 0 | disk | 
4 | 1 | 1 | 13
5 | 1 | 2 | 12
6 | 0 | disk | 
7 | 1 | 4 | 2
8 | 0 | disk | 
9 | 0 | disk | 
a | 1 | 3 | 9
b | 1 | 7 | 3
c | 0 | disk | 
d | 0 | disk | 
e | 1 | 0 | 10

## Slide 34: 34
0x0049
Frame/tag = 0x0
For each access, is it a hit in the TLB? no
Is it a hit in the page table? yes
A page fault? no
What is the updated page table?
What is the updated TLB?
Assume page sizes are 212 bytes
Virtual address space is 216 bytes, physical address space is 215 bytes
Virtual addresses are log(216) = 16 bits
Physical addresses are log(215) = 15 bits
Offset field = log(212) = 12 bits
Frame / Tag = 16-12 = 4 bits (virtual address)
Page = 15-12 = 3 bits (physical address)
Valid | Tag / Frame | Physical Page Number | Last Access time
1 | 0x5 | 2 | 12
1 | 0x2 | 6 | 11
1 | 0x0 | 5 | 14
1 | 0x4 | 1 | 13
Frame | Valid | Physical Page or in Disk | Last Access time
0 | 1 | 5 | 14
1 | 0 | disk | 
2 | 1 | 6 | 11
3 | 0 | disk | 
4 | 1 | 1 | 13
5 | 1 | 2 | 12
6 | 0 | disk | 
7 | 1 | 4 | 2
8 | 0 | disk | 
9 | 0 | disk | 
a | 1 | 3 | 9
b | 1 | 7 | 3
c | 0 | disk | 
d | 0 | disk | 
e | 1 | 0 | 10

## Slide 35: 35
0x0049
Frame/tag = 0x0
For each access, is it a hit in the TLB? no
Is it a hit in the page table? yes
A page fault? no
What is the updated page table?
What is the updated TLB?
Physical page number
0x5049 101 0000 0100 1001
Assume page sizes are 212 bytes
Virtual address space is 216 bytes, physical address space is 215 bytes
Virtual addresses are log(216) = 16 bits
Physical addresses are log(215) = 15 bits
Offset field = log(212) = 12 bits
Frame / Tag = 16-12 = 4 bits (virtual address)
Page = 15-12 = 3 bits (physical address)
Valid | Tag / Frame | Physical Page Number | Last Access time
1 | 0x5 | 2 | 12
1 | 0x2 | 6 | 11
1 | 0x0 | 5 | 14
1 | 0x4 | 1 | 13
Frame | Valid | Physical Page or in Disk | Last Access time
0 | 1 | 5 | 14
1 | 0 | disk | 
2 | 1 | 6 | 11
3 | 0 | disk | 
4 | 1 | 1 | 13
5 | 1 | 2 | 12
6 | 0 | disk | 
7 | 1 | 4 | 2
8 | 0 | disk | 
9 | 0 | disk | 
a | 1 | 3 | 9
b | 1 | 7 | 3
c | 0 | disk | 
d | 0 | disk | 
e | 1 | 0 | 10