## Slide 1: Computer Performance ISAs Benchmarking
CDA 3101 Discussion Slides
1 Sep 2022

## Slide 2: On the examlet
Performance equation
Average CPI
Calculating speed up
RISC vs CISC
Benchmarking
Parts of a computer

## Slide 3
Consider two different implementations of the same instruction set architecture. The instructions can be divided into four classes according to their CPI (class A, B, C, D). P1 has a clock rate of 2.5 GHz and CPIs of 1, 2, 3, and 3. P2 has a clock rate of 3 GHz and CPIs of 3, 3, 3, and 3.
Given a program with an instruction count of 1e6 divided into classes as follows: 10% class A, 20% class B, 50% class C, 20% class D, which is faster, P1 or P2?

## Slide 4
Consider two different implementations of the same instruction set architecture. The instructions can be divided into four classes according to their CPI (class A, B, C, D). P1 has a clock rate of 2.5 GHz and CPIs of 1, 2, 3, and 3. P2 has a clock rate of 3 GHz and CPIs of 3, 3, 3, and 3.
Given a program with an instruction count of 1e6 divided into classes as follows: 10% class A, 20% class B, 50% class C, 20% class D, which is faster, P1 or P2?
P1: CPIavg = 1* 0.1 + 2 * 0.2 + 3*0.5 + 3 * 0.2 = 2.6 cycles/instruction
tP1 =(1e6 instructions/program * 2.6 cycles/instruction)/2.5e9 cycles/second = 0.00104 seconds

## Slide 5
Consider two different implementations of the same instruction set architecture. The instructions can be divided into four classes according to their CPI (class A, B, C, D). P1 has a clock rate of 2.5 GHz and CPIs of 1, 2, 3, and 3. P2 has a clock rate of 3 GHz and CPIs of 3, 3, 3, and 3.
Given a program with an instruction count of 1e6 divided into classes as follows: 10% class A, 20% class B, 50% class C, 20% class D, which is faster, P1 or P2?
P1: CPIavg = 1* 0.1 + 2 * 0.2 + 3*0.5 + 3 * 0.2 = 2.6 cycles/instruction
tP1 =(1e6 instructions/program * 2.6 cycles/instruction)/2.5e9 cycles/second = 0.00104 seconds
P2: CPIavg = 3
tP2 = (1e6 instructions/program * 3 cycles/instruction)/3e9 cycles/second = 0.0010 seconds

## Slide 6
Consider two different implementations of the same instruction set architecture. The instructions can be divided into four classes according to their CPI (class A, B, C, D). P1 has a clock rate of 2.5 GHz and CPIs of 1, 2, 3, and 3.
Given a program with an instruction count of 1e6 divided into classes as follows: 10% class A, 20% class B, 50% class C, 20% class D.
P1: CPIavg = 1* 0.1 + 2 * 0.2 + 3*0.5 + 3 * 0.2 = 2.6 cycles/instruction
tP1 =(1e6 instructions/program * 2.6 cycles/instruction)/2.5e9 cycles/second = 0.00104 seconds
What is the speedup of P1 if the the clock rate is improved to 4 GHz?

## Slide 7
Consider two different implementations of the same instruction set architecture. The instructions can be divided into four classes according to their CPI (class A, B, C, D). P1 has a clock rate of 2.5 GHz and CPIs of 1, 2, 3, and 3.
Given a program with an instruction count of 1e6 divided into classes as follows: 10% class A, 20% class B, 50% class C, 20% class D.
P1: CPIavg = 1* 0.1 + 2 * 0.2 + 3*0.5 + 3 * 0.2 = 2.6 cycles/instruction
tP1 =(1e6 instructions/program * 2.6 cycles/instruction)/2.5e9 cycles/second = 0.00104 seconds
What is the speedup of P1 if the the clock rate is improved to 4 GHz?
Speedup = told/tnew = (IC*CPI/clockrate)old/(IC*CPI/clockrate)new
IC and CPI have not changed

## Slide 8
Consider two different implementations of the same instruction set architecture. The instructions can be divided into four classes according to their CPI (class A, B, C, D). P1 has a clock rate of 2.5 GHz and CPIs of 1, 2, 3, and 3.
Given a program with an instruction count of 1e6 divided into classes as follows: 10% class A, 20% class B, 50% class C, 20% class D.
P1: CPIavg = 1* 0.1 + 2 * 0.2 + 3*0.5 + 3 * 0.2 = 2.6 cycles/instruction
tP1 =(1e6 instructions/program * 2.6 cycles/instruction)/2.5e9 cycles/second = 0.00104 seconds
What is the speedup of P1 if the the clock rate is improved to 4 GHz?
Speedup = told/tnew = (IC*CPI/clockrate)old/(IC*CPI/clockrate)new = clockratenew/clockrateold =
(4e9cycles/instruction)/(2.5e9cycles/instruction) = 1.6

## Slide 9
Consider two different implementations of the same instruction set architecture. The instructions can be divided into four classes according to their CPI (class A, B, C, D). P1 has a clock rate of 2.5 GHz and CPIs of 1, 2, 3, and 3.
Given a program with an instruction count of 1e6 divided into classes as follows: 10% class A, 20% class B, 50% class C, 20% class D.
P1: CPIavg = 1* 0.1 + 2 * 0.2 + 3*0.5 + 3 * 0.2 = 2.6 cycles/instruction
tP1 =(1e6 instructions/program * 2.6 cycles/instruction)/2.5e9 cycles/second = 0.00104 seconds
What is the speedup of P1 if the the clock rate is improved to 4 GHz?
Speedup = told/tnew = (IC*CPI/clockrate)old/(IC*CPI/clockrate)new = clockratenew/clockrateold = 4/2.5 = 1.6

## Slide 10
Consider two different implementations of the same instruction set architecture. The instructions can be divided into four classes according to their CPI (class A, B, C, D). P1 has a clock rate of 2.5 GHz and CPIs of 1, 2, 3, and 3.
Given a program with an instruction count of 1e6 divided into classes as follows: 10% class A, 20% class B, 50% class C, 20% class D.
P1: CPIavg = 1* 0.1 + 2 * 0.2 + 3*0.5 + 3 * 0.2 = 2.6 cycles/instruction
tP1 =(1e6 instructions/program * 2.6 cycles/instruction)/2.5e9 cycles/second = 0.00104 seconds
What is the speedup of P1 if the the clock rate is improved to 4 GHz and class D instructions are improved to CPI=1?

## Slide 11
Consider two different implementations of the same instruction set architecture. The instructions can be divided into four classes according to their CPI (class A, B, C, D). P1 has a clock rate of 2.5 GHz and CPIs of 1, 2, 3, and 3.
Given a program with an instruction count of 1e6 divided into classes as follows: 10% class A, 20% class B, 50% class C, 20% class D.
P1: CPIavg = 1* 0.1 + 2 * 0.2 + 3*0.5 + 3 * 0.2 = 2.6 cycles/instruction
tP1 =(1e6 instructions/program * 2.6 cycles/instruction)/2.5e9 cycles/second = 0.00104 seconds
What is the speedup of P1 if the the clock rate is improved to 4 GHz and class D instructions are improved to CPI=1?
CPIavg = 1*0.1+2*0.2+3*0.5+1*0.2 = 2.2 cycles/instruction
Speedup = told/tnew = (IC*CPI/clockrate)old/(IC*CPI/clockrate)new = (CPI/clockrate)old / (CPI/clockrate)new
IC is the same

## Slide 12
Consider two different implementations of the same instruction set architecture. The instructions can be divided into four classes according to their CPI (class A, B, C, D). P1 has a clock rate of 2.5 GHz and CPIs of 1, 2, 3, and 3.
Given a program with an instruction count of 1e6 divided into classes as follows: 10% class A, 20% class B, 50% class C, 20% class D.
P1: CPIavg = 1* 0.1 + 2 * 0.2 + 3*0.5 + 3 * 0.2 = 2.6 cycles/instruction
tP1 =(1e6 instructions/program * 2.6 cycles/instruction)/2.5e9 cycles/second = 0.00104 seconds
What is the speedup of P1 if the the clock rate is improved to 4 GHz and class D instructions are improved to CPI=1?
CPIavg = 1*0.1+2*0.2+3*0.5+1*0.2 = 2.2 cycles/instruction
Speedup = told/tnew = (IC*CPI/clockrate)old/(IC*CPI/clockrate)new = (CPI/clockrate)old / (CPI/clockrate)new
= (2.6/2.5e9) / (2.2/4e9) = 1.89

## Slide 13
Consider two different implementations of the same instruction set architecture. The instructions can be divided into four classes according to their CPI (class A, B, C, D). P1 has a clock rate of 2.5 GHz and CPIs of 1, 2, 3, and 3.
Given a program with an instruction count of 1e6 divided into classes as follows: 10% class A, 20% class B, 50% class C, 20% class D.
P1: CPIavg = 1* 0.1 + 2 * 0.2 + 3*0.5 + 3 * 0.2 = 2.6 cycles/instruction
tP1 =(1e6 instructions/program * 2.6 cycles/instruction)/2.5e9 cycles/second = 0.00104 seconds
What is the speedup of P1 if the the clock rate is improved to 4 GHz and class D instructions are improved to CPI=1?
CPIavg = 1*0.1+2*0.2+3*0.5+1*0.2 = 2.2 cycles/instruction
Speedup = told/tnew = (IC*CPI/clockrate)old/(IC*CPI/clockrate)new = (CPI/clockrate)old / (CPI/clockrate)new
= (2.6/2.5) / (2.2/4) = 1.89

## Slide 14: RISC versus CISC
RISC
  Few types of instructions
  Simpler hardware
CISC
  Many types of instructions
  Complex hardware

## Slide 15: RISC versus CISC
RISC
  Few types of instructions
  Simpler hardware
CISC
  Many types of instructions
  Complex hardware
Few types of instructions means that high level language instructions (e.g. C) turn into many assembly language instructions.
RISC is best when applications are simple.

## Slide 16: RISC versus CISC
RISC
  Few types of instructions
  Compiles into longer programs
  Simpler hardware
CISC
  Many types of instructions
  Compiles into shorter programs
  Complex hardware
Lower power consumption and simple hardware makes RISC popular for small, portable (battery powered) devices, and for specialized devices.
ARM is a very popular RISC ISA

## Slide 17: RISC versus CISC
CISC is used for general-purpose platforms, like laptops. It’s good for platforms where users compile and run their own programs.
x86 is CISC
RISC
  Few types of instructions
  Compiles into longer programs
  Simpler hardware
CISC
  Many types of instructions
  Compiles into shorter programs
  Complex hardware

## Slide 18: Benchmarking
https://www.spec.org/cpu2017/results/

## Slide 19: Benchmarking

## Slide 20: Benchmarking
Geometric average of ratio values
On average, this platform is 200 times
faster than the baseline machine

## Slide 21: Benchmarking
Clock rate

## Slide 22
(© Morgan Kaufmann)
Notes: OFF SCREEN
This slide shows the five main components of a computer: input, output, memory, datapath, and control. [CLICK]
Input writes data [CLICK] and instructions in memory. [CLICK]
The datapath gets data and instructions from memory. [CLICK]
Control sends signals that determine the operations of the datapath, memory, input and output.
[CLICK – Next Slide]

## Slide 23
(© Morgan Kaufmann)
Input writes data and instructions in memory
Notes: OFF SCREEN
This slide shows the five main components of a computer: input, output, memory, datapath, and control. [CLICK]
Input writes data [CLICK] and instructions in memory. [CLICK]
The datapath gets data and instructions from memory. [CLICK]
Control sends signals that determine the operations of the datapath, memory, input and output.
[CLICK – Next Slide]

## Slide 24
(© Morgan Kaufmann)
Datapath executes instructions
Notes: OFF SCREEN
This slide shows the five main components of a computer: input, output, memory, datapath, and control. [CLICK]
Input writes data [CLICK] and instructions in memory. [CLICK]
The datapath gets data and instructions from memory. [CLICK]
Control sends signals that determine the operations of the datapath, memory, input and output.
[CLICK – Next Slide]

## Slide 25
(© Morgan Kaufmann)
Control sends signals that determine the operations of datapath, memory, input and output
Notes: OFF SCREEN
This slide shows the five main components of a computer: input, output, memory, datapath, and control. [CLICK]
Input writes data [CLICK] and instructions in memory. [CLICK]
The datapath gets data and instructions from memory. [CLICK]
Control sends signals that determine the operations of the datapath, memory, input and output.
[CLICK – Next Slide]

## Slide 26
(© Morgan Kaufmann)
Stores instructions and data
Notes: OFF SCREEN
This slide shows the five main components of a computer: input, output, memory, datapath, and control. [CLICK]
Input writes data [CLICK] and instructions in memory. [CLICK]
The datapath gets data and instructions from memory. [CLICK]
Control sends signals that determine the operations of the datapath, memory, input and output.
[CLICK – Next Slide]

## Slide 27
(© Morgan Kaufmann)
Presents results to user
Notes: OFF SCREEN
This slide shows the five main components of a computer: input, output, memory, datapath, and control. [CLICK]
Input writes data [CLICK] and instructions in memory. [CLICK]
The datapath gets data and instructions from memory. [CLICK]
Control sends signals that determine the operations of the datapath, memory, input and output.
[CLICK – Next Slide]