## Slide 1: ARM Instructions Sample Problems
CDA 3101

## Slide 2: What’s on the examlet?
Sum of products / product of sums
Specialty circuits
  Multiplexor, Decoder, Majority, Comparator
Translate from ARM machine code to assembly and vice versa

## Slide 3: ARM ISA: R-format instruction
STRUCTURE OF AN R-format INSTRUCTION
Instruction Fields:
Field Explanation:
  opcode - basic operation of the instruction
  rm – second source register
  shamt – shift amount
  rn – first source register
  rd destination register
opcode rm shamt rn rd
11 bits 5 bits 6 bits 5 bits 5 bits

## Slide 4: Sample problem
What is the 32 bit machine code corresponding to
LSL X10, X9, #3
(Look at reference sheet)
Opcode = 11010011011, Format = R

## Slide 5: Sample problem
What is the 32 bit machine code corresponding to
LSL X10, X9, #3
(Look at reference sheet)
Opcode = 11010011011, Format = R, Rn is shifted and placed in Rd

## Slide 6: Sample problem
What is the 32 bit machine code corresponding to
LSL X10, X9, #3
(Look at reference sheet)
Opcode = 11010011011, Format = R, RN shifted and placed in RD
11010011011 00000 000011 01001 01010
Rm is not used
shamt = shift amount = 3
Rd
Rn

## Slide 7: Sample problem
What is the 32 bit machine code corresponding to
LSL X10, X9, #3
(Look at reference sheet)
Opcode = 11010011011, Format = R, RN shifted and placed in RD
11010011011 00000 000011 01001 01010
11010011011000000000110100101010
1101 0011 0110 0000 0000 1101 0010 1010
0xD3600D2A

## Slide 8: ARM ISA: R-format instruction
ADD X9, X10, X11  X9 = X10+X11
opcode rm shamt rn rd
11 bits 5 bits 6 bits 5 bits 5 bits
10001011000 01011 000000 01010 01001
SUB X9, X10, X11  X9 = X10-X11
opcode rm shamt rn rd
11 bits 5 bits 6 bits 5 bits 5 bits
11001011000 01011 000000 01010 01001

## Slide 9: ARM ISA: I-format instruction
STRUCTURE OF AN I-format INSTRUCTION
Instruction Fields:
Field Explanation:
  opcode - basic operation of the instruction
  Immediate – value of operand
  rn – source register
  rd destination register
opcode immediate rn rd
10 bits 12 bits 5 bits 5 bits

## Slide 10: ARM ISA: I-Type Instructions
ADDI X9, X10, #100  X9 = X10-100
opcode immediate rn rd
10 bits 12 bits 5 bits 5 bits
1001000100 000001100100 01010 01001

## Slide 11: Sample Problem
What is the ARM instruction corresponding to
0xF8008269
1111 1000 0000 0000 1000 0010 0110 1001
(look at reference sheet)

## Slide 12: Sample Problem
What is the ARM instruction corresponding to
0xF8008269
1111 1000 0000 0000 1000 0010 0110 1001
(look at reference sheet)
Opcode starts with 11111, so it is LDUR or STUR
These are both D type
11111000000 000001000 00 10011 01001
STUR X9, [X19, #8]

## Slide 13: Sample Problem
What is the ARM instruction corresponding to
0xF8008269
1111 1000 0000 0000 1000 0010 0110 1001
(look at reference sheet)
Opcode starts with 11111, so it is LDUR or STUR
These are both D type
11111000000 000001000 00 10011 01001
STUR X9, [X19, #8]

## Slide 14: Sample Problem
What is the ARM instruction corresponding to
0x14000060
0001 0100 0000 0000 0000 0000 0110 0000
(look at reference sheet)

## Slide 15: Sample Problem
What is the ARM instruction corresponding to
0x14000060
0001 0100 0000 0000 0000 0000 0110 0000
(look at reference sheet)
000101 = B
B instruction has two fields: opcode and address
000101 00000000000000000001100000
B #96