## Slide 1: CDA3101
Module 3: ARM Procedures (Part 4)

## Slide 2: Welcome!
Notes: ON SCREEN
Welcome back to CDA3101, Module 3. In this video, we’re going to learn how to write recursive procedures in ARM
[CLICK – Next Slide]

## Slide 3: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame, SP = X28 = stack pointer
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
Here we have the high level code for calculating factorial
The ARM code will start with the label for the procedure. Our fact procedure has one argument, n, and it will be in register x0
First we will determine if n is greater than 1.
[CLICK – Next Slide]

## Slide 4: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame, SP = X28 = stack pointer
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
We’ll do that by subtracting 1 from n and setting the flags. Then we call B.GT
[CLICK – Next Slide]

## Slide 5: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame, SP = X28 = stack pointer
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
If n is greater than 1, we branch to the recursive part of the code.
Next is the code for the base case.
[CLICK – Next Slide]

## Slide 6: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame, SP = X28 = stack pointer
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
If we haven’t branched to the recursive case, we perform the base case. [CLICK]
The base case is simply to return 1.
[CLICK – Next Slide]

## Slide 7: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
MOV X1, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame, SP = X28 = stack pointer
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
The return value needs to be in register X1, so we will put a value of 1 in register X1
[CLICK – Next Slide]

## Slide 8: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
MOV X1, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame, SP = X28 = stack pointer
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
And call BR X30, which branches to the address found in register X30
Now we’re going to set up a recursive call to fact with an argument of n-1 [CLICK]
Before we recursively call our procedure, we need to set up a stack frame.
On the stack frame we need to save the argument x0, and the return address, because they will get overwritten when we make a procedure call.
[CLICK – Next Slide]

## Slide 9: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
MOV X1, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame, SP = X28 = stack pointer
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
So we will make room on the stack for two variables by subtracting 16 from the stack pointer.
[CLICK – Next Slide]

## Slide 10: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
MOV X1, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame, SP = X28 = stack pointer
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
We’ll store the value in register X30 on the stack,
[CLICK – Next Slide]

## Slide 11: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
MOV X1, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame, SP = X28 = stack pointer
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
and we’ll store the value in register X0 on the stack.
Before we call our procedure, we need to update the argument register X0.
[CLICK – Next Slide]

## Slide 12: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame, SP = X28 = stack pointer
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
The high level code says we recursively call with n-1 as an argument
[CLICK – Next Slide]

## Slide 13: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
MOV X1, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame, SP = X28 = stack pointer
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
n is in register X0, so we subtract 1 from it
[CLICK – Next Slide]

## Slide 14: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
MOV X1, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame, SP = X28 = stack pointer
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
then we branch and link to fact, recursively calling the fact procedure
[CLICK – Next Slide]

## Slide 15: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
MOV X1, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame, SP = X28 = stack pointer
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
When our recursive call is done, execution continues on with next instruction
The value that our recursive call calculated is in the register X1
[CLICK – Next Slide]

## Slide 16: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
MOV X1, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame, SP = X28 = stack pointer
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
After returning from the recursive procedure call, we restore the values we saved on the stack back into registers
We load the value of n back into register x0
[CLICK – Next Slide]

## Slide 17: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
MOV X1, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame, SP = X28 = stack pointer
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
We load the return address back into x30
[CLICK – Next Slide]

## Slide 18: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
MOV X1, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame, SP = X28 = stack pointer
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
And we remove the stack frame by moving the stack pointer up
Now we have to multiply the value returned from the recursive call by n
[CLICK – Next Slide]

## Slide 19: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
MOV X1, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame, SP = X28 = stack pointer
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
The value returned from the call to factorial with an argument of n-1 is in register X1
[CLICK – Next Slide]

## Slide 20: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
MOV X1, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame, SP = X28 = stack pointer
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
So we multiply the value returned by the previous call, in X1 by n, in X0, and place it in register X1
[CLICK – Next Slide]

## Slide 21: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
MOV X1, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame, SP = X28 = stack pointer
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
Then we return via a branch to register X30.
And there you have it! One line of high level code turned into 14 lines of machine code!
Let’s do a run through the code
[CLICK – Next Slide]

## Slide 22: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
SP
fact(3)
X0: 3
X30: 0x500000
Main
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
MOV X1, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
Let’s call the procedure fact with an argument of 3. [CLICK]
We will be calculating the factorial of 3. [CLICK]
When the code is first entered, and execution commences at the “fact:” label, X0 has a value of 3. [CLICK]
For the sake of example, we are going to say that X30, the return address, currently has the value shown.
[CLICK – Next Slide]

## Slide 23: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
SP
Main
fact(3)
X0: 3
X30: 0x500000
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
When the sub and set flags is executed, we find that x0 minus 1 is not zero.
So the B.gt instruction jumps to the recurse label
[CLICK – Next Slide]

## Slide 24: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
SP
Main
fact(3)
X0: 3
X30: 0x500000
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
Next we run this instruction to create the stack frame.
[CLICK – Next Slide]

## Slide 25: Recursion
SP
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
Main
fact(3)
X0: 3
X30: 0x500000
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
And these instructions to save the current values in X0 and X30 into the stack frame
[CLICK – Next Slide]

## Slide 26: Recursion
3
0x500000
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
Main
SP
fact(3)
X0: 3
X30: 0x500000
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
[Allow animations to finish and click to next slide]

## Slide 27: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
3
0x500000
Main
SP
fact(3)
X0: 3
X30: 0x500000
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
Now we subtract 1 from n, since that is the argument for our next procedure call
[CLICK – Next Slide]

## Slide 28: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
3
0x500000
Main
SP
fact(3)
X0: 2
X30: 0x500000
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
X0 now contains 2
[CLICK – Next Slide]

## Slide 29: Recursion
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
0x50000F
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
3
0x500000
Main
SP
fact(3)
X0: 2
X30: 0x500000
Notes: OFF SCREEN
For the sake of example, let’s say the instruction after the procedure call has the address shown
[CLICK – Next Slide]

## Slide 30: Recursion
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
3
0x500000
Main
SP
fact(3)
X0: 2
X30: 0x500000
0x50000F
Notes: OFF SCREEN
When we call branch and link to fact, this value is placed in X30
[CLICK – Next Slide]

## Slide 31: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
3
0x500000
Main
SP
fact(3)
X0: 2
X30: 0x50000F
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
Since we called branch and link to fact, execution continues at the fact label
[CLICK – Next Slide]

## Slide 32: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
3
0x500000
Main
SP
fact(2)
X0: 2
X30: 0x50000F
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
the sub and set flags is executed and compares x0, which contains a value of 2, and 1.
[CLICK – Next Slide]

## Slide 33: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
3
0x500000
Main
SP
fact(2)
X0: 2
X30: 0x50000F
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
Since x0 is greater than 1, we branch to the recurse label
[CLICK – Next Slide]

## Slide 34: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
3
0x500000
Main
SP
fact(2)
X0: 2
X30: 0x50000F
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
Another stack frame is created before the next recursive procedure call is made.
[CLICK – Next Slide]

## Slide 35: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
3
0x500000
Main
SP
fact(2)
X0: 2
X30: 0x50000F
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
The current values in X0 and X30 are saved into this stack frame
[CLICK – Next Slide]

## Slide 36: Recursion
2
0x50000F
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
3
0x500000
Main
SP
fact(2)
X0: 2
X30: 0x50000F
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
[Allow animations to finish and click to next slide]

## Slide 37: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
2
0x50000F
3
0x500000
Main
SP
fact(2)
X0: 2
X30: 0x50000F
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
Before we call fact again, we adjust the argument. We subtract 1 from n, so it is now equal to 1.
[CLICK – Next Slide]

## Slide 38: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
2
0x50000F
3
0x500000
Main
SP
fact(2)
X0: 1
X30: 0x50000F
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
And we do another branch and link to factorial. Our next recursive call.
[CLICK – Next Slide]

## Slide 39: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
2
0x50000F
3
0x500000
Main
SP
fact(1)
X0: 1
X30: 0x50000F
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
After the branch and link, execution continues at the fact label
Again we compare x0 to 1. The value in X0 is 1. We have reached the base case and don’t branch to recurse
[CLICK – Next Slide]

## Slide 40: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
X1: 1
2
0x50000F
3
0x500000
Main
SP
fact(1)
X0: 1
X30: 0x50000F
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
MOV X1, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
We execute the base case by placing 1 in the x1 register to return 1 [CLICK]
We then execute a branch to the address in register x30.
The values in the registers are shown here
[CLICK – Next Slide]

## Slide 41: Recursion
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
MOV X1, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
2
0x50000F
3
0x500000
Main
SP
X1: 1
fact(1)
X0: 1
X30: 0x50000F
0x50000F
Notes: OFF SCREEN
When we branch to the value in X30, we’re going to branch to here
[CLICK – Next Slide]

## Slide 42: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
2
0x50000F
3
0x500000
Main
SP
X1: 1
fact(1)
X0: 1
X30: 0x50000F
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
Execution continues at the instruction at the address in x30 [CLICK]
First we get a value off the stack and put it in register x0.
[CLICK – Next Slide]

## Slide 43: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
2
0x50000F
3
0x500000
Main
SP
X1: 1
fact(2)
X0: 2
X30: 0x50000F
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
So now x0 has a value of 2. This is the value it had BEFORE the last recursive call. [CLICK]
We get the next value off the stack and put it in register X30.
[CLICK – Next Slide]

## Slide 44: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
2
0x50000F
3
0x500000
Main
SP
X1: 1
fact(2)
X0: 2
X30: 0x50000F
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
Now we move the stack pointer by adding 16 to it.
[CLICK – Next Slide]

## Slide 45: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
3
0x500000
Main
SP
X1: 1
fact(2)
X0: 2
X30: 0x50000F
2
0x50000F
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
[Allow animations to finish and click to next slide]

## Slide 46: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
3
0x500000
Main
SP
X1: 1
fact(2)
X0: 2
X30: 0x50000F
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
Now we multiply the value in X1 that was returned by the last recursive call, 1, by the value in X0, 2 to get X1 = 2
[CLICK – Next Slide]

## Slide 47: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
3
0x500000
Main
SP
X1: 2
fact(2)
X0: 2
X30: 0x50000F
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
[Allow animations to finish and click to next slide]

## Slide 48: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
3
0x500000
Main
SP
X1: 2
fact(2)
X0: 2
X30: 0x50000F
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
And we branch to the address in register x30
[CLICK – Next Slide]

## Slide 49: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
3
0x500000
Main
SP
X1: 2
fact(2)
X0: 2
X30: 0x50000F
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
And we are back at this address.
And copying data from the stack.
The value now at the top of the stack [CLICK] is placed into X0
[CLICK – Next Slide]

## Slide 50: Recursion
2
0x50000F
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
3
0x500000
Main
SP
X1: 2
fact(3)
X0: 3
X30: 0x50000F
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
And the next value on the stack [CLICK] is placed into X30
[CLICK – Next Slide]

## Slide 51: Recursion
2
0x50000F
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
3
0x500000
Main
SP
X1: 2
fact(3)
X0: 3
X30: 0x500000
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
We remove the stack frame from the stack by moving the stack pointer
[CLICK – Next Slide]

## Slide 52: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
SP
Main
X1: 2
fact(3)
X0: 3
X30: 0x500000
3
0x500000
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
[Allow animations to finish and click to next slide]

## Slide 53: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
SP
Main
X1: 2
fact(3)
X0: 3
X30: 0x500000
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
Then we multiply the value currently in X1, 2, by the value in X0, 3, and place the result, 6 in X1.
[CLICK – Next Slide]

## Slide 54: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
SP
Main
X1: 6
fact(3)
X0: 3
X30: 0x500000
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
We now branch to the value in X30, which is the address we made the first call from.
[CLICK – Next Slide]

## Slide 55: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
SP
Main
X1: 6
fact(3)
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
ADD X1, XZR, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
And our return value is 6.
Which is indeed the factorial of 3.
[CLICK – Next Slide]

## Slide 56: Recursion
High Level Language
long long int fact(long long int n)
{
if(n<=1) return 1 else return n*fact(n-1);
}
SP
Main
X1: 6
fact(3)
FACT: //argument is in X0
SUBS X9, X0, #1
B.GT RECURSE
//base case
MOV X1, #1 //return argument X1 is 1
BR X30 //return
RECURSE: SUB SP, SP, #16 //prepare stack frame
STUR X30, [SP, #8] //save return address
STUR X0, [SP, #0] //save argument n
SUB X0, X0, #1 //recursive call will have n-1 as argument
BL FACT //call fact with n-1
//return from recursive call, fact(n-1) is in X1
LDUR X0, [SP, #0] //restore n
LDUR X30, [SP, #8] //restore return address
ADD SP, SP, #16 //restore stack pointer
MUL X1, X0, X1 //value to be returned = n*fact(n-1)
BR X30 //return
Notes: OFF SCREEN
You can now see that every recursive call causes data to be saved in dynamic memory. You can see why recursion is expensive, and why infinite recursion crashes your computer. Eventually you run out of memory.
[CLICK – Next Slide]

## Slide 57: Wrap Up
Notes: ON SCREEN
Thanks for watching! That’s going to end this video.
[CLICK – Next Slide]

## Slide 58: Thank you for watching.